## Slide 1: IALA Input paper ENG14- 3.1.3.2 Galileo Timing for R-Mode – Testing campaign
IALA ENG14
8 October 2021

## Slide 2: Introduction
Objectives
Carried out under GSALOT3TRANS, Specific Contract 10 project funded by EUSPA (GSA/OP/09/16/Lot 3/SC10). This Contract aims at provide technical and business consulting and operational assistance in all matters related to the implementation of the EGNSS adoption roadmap in the area of transport applications.
The pilot goal is to analyse the suitability of Galileo Timing for R-Mode considering the analysis of Galileo capabilities for timing purposes.
The consortium is composed by:
    GMV, technical leader
    VVA, market and economic leader
    Support from R-Mode Baltic project partners (German Federal Waterways Administration WSV and German Aerospace Center DLR)

## Slide 3: Context of the study
R-Mode
R-Mode (Ranging Mode) technology is being developed in the frame of maritime community as a terrestrial backup positioning system for maritime and inland waterways navigation in case any of GNSS vulnerabilities takes place as jamming and spoofing.
R-Mode allows calculating user receiver position in relation to fixed-shore and synchronized radio transmitters.
Examples: ACCSEAS (assumed perfect synchronization among nodes), R-Mode Baltic (GPS-based solutions)

## Slide 4: Context of the study
Galileo
Available since 2016 (initial services)
Galileo provides greater precision than other available system, has higher availability, increases GNSS coverage by being interoperable with other systems, provides emergency-response services, etc.
Galileo contributes to improve the accuracy performance of GNSS users, including the time and synchronization community. Galileo satellites may also improve integrity and ensure availability of the timing service in case other GNSS constellation experiences outages.
As already presented in ENG10, GSALOT3TRANS-SC3 study concluded that Galileo is promising technology to be considered as a cost-effective alternative to the use of atomic clocks for R-Mode infrastructure synchronization.

## Slide 5: Galileo Timing for R-Mode Pilot Project
Methodology
Step 1: Prepare and implement a Pilot project in cooperation with interested authorities, (e.g. R-Mode Baltic project).
Step 2: Assess the suitability of performances and identification of user requirements
Step 3: Deliver a description of the suitable infrastructure and practical guidelines to implement Galileo timing in R-Mode.

## Slide 6: Galileo Timing for R-Mode Pilot Project
Set-up
GALILEO TIMING RECEIVER
R-Mode stations (WSV)
R-Mode user receiver (DLR)
(Groß Königsförde)
Source: DRAFT on Implementation of R-Mode on MF
Galileo receiver
Output 1: 1PPS
Output 2: 10 MHz

## Slide 7: Galileo Timing for R-Mode Pilot Project
Galileo Timing Receiver requirements
Guaranteed precision can only be obtained using dual-frequency GNSS receivers, which is not very common in industrial timing receivers.
Guaranteed precision can only be obtained from GNSS receivers that allow to “fix” the antenna position to accurate coordinates.
The receiver must allow the user to enter the calculated total delay and to advance the 1PPS accordingly. This is not a standard feature in existing receivers
 | GMV WanTime
Dual frequency | 
Multiconstellation | 
Fixing of the antenna position | 
Fixing of total delay | 
1PPS out Jitter | <100 ps
1PPS Accuracy (1-sigma) | <2 ns

## Slide 8: Galileo Timing for R-Mode Pilot Project
Timing KPIs case studies
To be measured at laboratory due to the need of an stable timing reference to UTC Time Scale
Minimum one week of data
Timing KPIs
MTIE - Maximum time interval error
TDEV - Time stability

## Slide 9: Galileo Timing for R-Mode Pilot Project
Positioning KPIs case studies
  To be measured at the field
  4 weeks of data
  Holdover must be considered
  Case-studies:
  Full dataset
  Full dataset separated per day
  Day time and night time data
    It may degrade the performance
  Scenarios
  Error statistics with holdover
  Error statistics removing epochs where holdover is enabled

## Slide 10: Galileo Timing for R-Mode Pilot Project
Positioning KPIs
Directly obtained from R-Mode receiver
    Position
    Position error
    Pseudorange
    Bias
  Directly obtained from WANTime receiver
    Datalogs informing whether holdover has been activated, with the corresponding time stamp.
  Post-processed data
    Pseudorange error
    Availability
    Continuity
  Maximum value
  Mean
  95th percentile error

## Slide 11: AOB?

## Slide 12
Thank you for your attention
Gema Cueto-Felgueroso
gcueto@gmv.com

## Slide 13: Galileo Timing for R-Mode Pilot Project
GMV WANTime Receiver
GMV Tallysman 7972 Antenna
GMV WANTime Receiver
Installed Trimble Zephyr 3 Antenna
GMV Calibrated GNSS Receiver
Counter
GMV Calibrated Antenna
Groß Mohrdorf / Helgoland
Zeven
Due to the nature of these stations, GMV will provide the GNSS antenna and cable to be connected to the WANTime (best technical approach)
In this station, there is no way to use our own antenna and cable (GNSS antennas are on the top of a mast) so GMV will use the already installed antenna+cable and calibrate them .