## Slide 1
Maritime Cloud
A technical infrastructure to support seamless information transfer
in e-navigation
IALA e-NAV14 – September 2013
Ole Bakman Borup
Danish Maritime Authority
Maritime technology and e-navigation
Notes: Good afternoon, and thank you Mr. Chairman for this opportunity.
My name is Ole Borup, I work with the Danish Maritime Authority in the area of AIS and e-navigation development.
I have been involved in testbed implementations in the EfficienSea project and currently in the ACCSEAS project.
I would like to introduce a proposed technical infrastructure for e-navigation called the Maritime Cloud.
Next slide!

## Slide 2: Background
The overarching e-navigation architecture, decided by IMO, assumes seamless data exchange between maritime actors onboard and ashore
Testbed experience with potential e-navigation solutions has shown a need for a technical infrastructure to support this data exchange
Notes: The background for this infrastructure is
Firstly that the overarching e-navigation architecture, decided by IMO, assumes seamless data exchange between maritime actors onboard and ashore,
Secondly: testbed experience with potential e-navigation solutions has shown us a need for a technical infrastructure to support this data exchange

## Slide 3: Identified infrastructure requirements
New communication means
Service consumers must easily be able to locate provided services in an area
Service providers must easily be able to register their provided services
All maritime actors must have a unique maritime ID with attached attributes as role and nationality, etc.
Means for secure communication
  Authenticity – Guarantee of who I am talking to
  Integrity – Guarantee that data is unaltered
  Confidentiality – Guarantee that data is not accessible by third party
Notes: Early on a number of high-level requirements was identified and has driven the development of the infrastructure
New communication means to meet the requirements of e-navigation
The ability of service consumers to be able to locate provided services in an area
On the other hand service providers must easily be able to register their provided services
All maritime actors must have a unique maritime ID with attached attributes as role and nationality, etc.
The infrastructure must provide means for secure communication, that is to support
  Authenticity – Guarantee of who I am talking to
  Integrity – Guarantee that data is unaltered
  Confidentiality – Guarantee that data is not accessible by third party

## Slide 4: The Maritime Cloud – overview
Connects all maritime actors in a communication framework
Can be seen as refinement of the overarching architecture
  Not detailed ship or shore side architecture, but a component in CSSA and the ship side architecture
Consists of three key components
MMS
MMS
MMS
VTS, MRCC, Port, Shipowner…
Maritime
Identity
Registry
Maritime
Service
Portfolio
Registry
Notes: Our solution to meet these requirements, among others, was named the Maritime Cloud.
The Maritime Cloud connects all maritime actors in a communication framework.
It can be seen as a refinement of the overarching e-navigation architecture. But important to make it clear that it is not a detailed ship or shore architecture, but rather a component in the Common Shore-based System Architecture and the ship side architecture.
Consists of three key components:
Communication means – that is how to exchange data
a Maritime Identity registry – how to identify actors and solve security concerns
and a Maritime Service Portfolio Registry – how to locate provided services

## Slide 5: Communication
Digital communication means are essential for a communication framework
Currently we have only one general purpose digital communication mean universally available
  AIS ASM
In some cases we have
  Commercially available Internet (TCP/IP) (not necessarily accessible by navigation equipment)
  Stand alone text based or limited data package transfer systems via satellite or HF
Questionable if AIS ASM will be sufficient for the prioritized e-navigation solutions
New dedicated communication systems (like NAVDAT and VDES) need to be developed and demonstrated before they can be assumed – i.e. not available in the short term.
The cloud must be able to utilize different communication technologies
Notes: The first key component is communication. Digital communication means are of course essential for a communication framework.
Currently we have only one general purpose digital communication mean universally available
AIS ASM
In some cases we have
  Commercially available Internet (TCP/IP) (not necessarily accessible by navigation equipment)
  Standalone text based or limited data package transfer systems via satellite or HF
Questionable if AIS ASM will be sufficient for the prioritized e-navigation solutions
New dedicated communication systems (like NAVDAT and VDES) need to be developed and demonstrated before they can be assumed – i.e. not available in the short term.
BUT, the cloud must be able to utilize these different communication technologies as they become available

## Slide 6: Geo-messaging
Geo-aware messaging protocol on top of TCP/IP (overlay network)
Actors connects to a Maritime Messaging Server (MMS) to send and receive messages, and send position at a protocol level
The servers maintain a geographical awareness of actors
Can be supplemented by AIS data
Any available Internet connection can be used (prioritized)
Resilience by store and forward functionality
MMS
MMS
MMS
VTS, MRCC, Port, Shipowner…
Notes: In the need of new communication means and as we anticipate Internet to become an important communication mean in e-navigation, we propose a new geo-aware messaging protocol implemented on top of TCP/IP as part of the maritime cloud. We can also call that an overlay network to the Internet.
The protocol works by actors connecting to one among a number of Maritime Messaging Servers organized in a peer-to-peer network. When connected to the messaging server, the actor can send and receive messages, and at a protocol level the actor will regularly send its position in case of a mobile actor like a vessel.
This allows the servers to maintain a geographical awareness that they share among each other in a distributed fashion.
The geographical awareness could possibly be supplemented by AIS data
The protocol requires an Internet connection. In some cases a number of connections are available so the selection could be based on least cost routing or other prioritization.
Internet connections on vessels are often unstable, so to achieve resilience, the messaging servers will implement store and forward by caching messages that cannot be delivered and send them once an actor re-connects. Messages will have a time-to-live to indicate for how long messages are valid, and the cache will have priority queuing to send the most important messages first.

## Slide 7: Geo-messaging – features
Actors can send messages directly to other actors (no range limitations)
Geographical awareness enables geocasting (broadcast to given area)
Actors can listen to a specified area – or a specific service
Geocast is an implicit feature of many radio based communication systems
Emulation of current and future communication systems
Listens
Broadcasts
Listen – or Geocast
VTS, MRCC,
Port…
Notes: The geo-messaging protocol allows actors to send messages directly to other actors without any range limitation. The actors could be located at opposite sides of the globe.
Geographical awareness enables geocasting, that is actors can broadcast to other actors within a specified area
Actors can listen to a specified area – or a specific service. For example will non-mobile actors like a VTS not have a position, but will specify an area of interest for which they will receive messages
When we look at geocast we see that it is an implicit feature of many radio based communication systems. The area is not specified but given by the physical capabilities of the communication system. For example
AIS where the area will bounded by the range of the VHF signal.
In that sense we can use the geo-messaging protocol as a way to emulate current and future communication systems.
This will allow us in testbeds to identify communication requirements for potential e-navigation services without actually having to deploy the communication systems.

## Slide 8: Maritime Identity Registry
Distributed registry maintained by a number of identity brokers in a peer-to-peer network
All actors in e-navigation will obtain a Maritime Identity in the Maritime Identity Registry
  Similar to callsign or MMSI but not tied to role or specific technology
Security through public-key infrastructure
  All actors will obtain a digital certificate (with variable trust)
The registry contains information about the actors
  Static information (e.g. contact information, callsign, comm. capabilities etc.)
  Maybe also dynamic information integral for e-navigation (e.g. position and voyage information)
Notes: The second key component in the maritime cloud, is the Maritime Identity Registry,
It is a distributed registry maintained by a number of identity brokers in a peer-to-peer network.
All actors in e-navigation will obtain a Maritime Identity in the Maritime Identity Registry
  Similar to callsign or MMSI number but not tied to a specific role or specific technology
All actors will also obtain a digital certificate allowing to implement security in the cloud using a public-key infrastructure. The certificates will have variable trust. It is easy to obtain a certificate with low trust, but obtaining a certificate with a high level of trust, requires a process in which the actors identity is determined securely. Actors providing services will need a certificate with a high level of trust.
This completely resembles obtaining a certificate for your web site in the Internet domain.
The registry contains information about the actors.
Some is static information like contact information, callsign, communication capabilities, etc.
The registry could contain dynamic information considered integral for e-navigation, for example position and maybe voyage information.

## Slide 9: Maritime Service Portfolio Registry
Distributed registry maintained by a number of service brokers in a peer-to-peer network
Contains a service specification register and a service instance register
The specification of a service is envisioned to be located in the product specification part of the IHO S-100 GI Registry
The service instance register links
  Service (specification)
  Service provider (identity)
  Area / leg / junction where the service is offered
  Metadata like quality and service endpoints
Service providers maintain their provided services in the instance register
Service consumers make queries for available services
All actors can act as both service providers and consumers
Spans all maritime services
Notes: The third key component is the Maritime Service Portfolio Registry.
It’s a distributed registry maintained by a number of service brokers in a peer-to-peer network.
It contains a service specification register and a service instance register
The specification of a service is envisioned to be located in the product specification part of the IHO S-100 GI Registry
The service instance register will link
  Service (specification)
  Service provider (identity)
  Area / leg/junction where the service is offered
  Metadata like quality and service endpoints for different communication means
Service providers maintain their provided services in the instance register
Service consumers make queries for available services
All actors can act as both service providers and service consumers. A ship could for example provide sensor readings as a service. In this case the area where the service is provided would be relative to the ships position.
The Maritime Service Portfolio Registry is intended to span all maritime services, not just electronic services.

## Slide 10: Almanac
Offline version of the public part of Maritime Identity Registry and Maritime Service Portfolio Registry
Comparable to an advanced electronic “white pages / yellow pages” phonebook
Updated regularly (downloaded or carried onboard)
Identity and service concepts available offline
  Identities can be authenticated
  Data encryption for full confidentiality
  Find contact information etc. for actors
  Find provided services for areas
  Etc.
MRCC
Reykjavik
Thorshavn
…
SHIPS
ENRICO III
EMA MAERSK
ESVAGT ALPHA
…
VTS
Brevik VTS
Fejde VTS
…
WEATHER
Danish Meterological Institute
…
Ports
Aberdeen
Amsterdam
…
Notes: An important enabler of the Maritime Cloud is the Almanac.
It is an offline version of the public part of the Maritime Identity Registry and Maritime Service Portfolio Registry.
Its comparable to an advanced electronic “white pages / yellow pages” phonebook.
Actors can either use the registries directly using web services over the Internet, or have the offline almanac which needs to be updated regularly. Either downloaded when a connection is available, or carried onboard on a physical medium. This resembles how electronic navigational charts are kept up-to-date today.
Having the almanac allows offline use of the identity and service concepts, that is for example:
Other actors identities can be authenticated
Data can be encrypted for full confidentiality
Contact information and other information for actors can be located
Provided services in an area can be found
Etc

## Slide 11: Use case: Improved VTS communication
Automatic reporting based on IMO FAL forms
Shore – shore Inter VTS reporting (IVEF) – or via existing systems (SafeSeaNet, eNOA/D, etc.) will reduce broadband communication cost for shipping
MMS
MMS
MMS
VTS
VTS
VTS
PORT
SafeSeaNet,
eNOA/D, etc.
VTS REPORTING
IMO FAL FORMS
INTER VTS REPORTING
(IVEF)
Notes: To give an example on the use of the Maritime Cloud, we can see how VTS communication could be improved.
A vessel will be able to find contact information for VTS in an area and the services provided by the VTS can be located
The vessels will then be able to do for example reporting in full confidentiality and both parties will be assured of the identity of the other
Likewise would shore stakeholders be able to locate services provided by each other, for example IVEF, and be able to communicate securely. The Maritime Cloud does not mandate how to communicate, so Internet protocols can still be used, but augmented with the security concepts provided by the cloud
Sharing policies between stakeholders can be enforced by having authenticated identities. We know who we give information to.

## Slide 12: Use case: MSI promulgation - Current solution
Broadcast
MSI provider
NAVTEX
SAFETYNET (INMARSAT)
???
???
Receiver manfunction
Region of relevance
Notes: Another example on the use of the cloud, is how the promulgation of maritime safety information can be improved with new communication means.
This is the current situation:
Maritime Safety Information may have an region of relevance, but current promulgation like NAVTEX and Safetynet have coverage based on physical capabilities.
The communication is one way, so there is no guarantee if the relevant vessels receive the messages.

## Slide 13: MSI promulgation: Current result
Broadcast
MSI provider
NAVTEX
SAFETYNET (INMARSAT)
???
???
Receiver manfunction
Region of relevance
Notes: This is the current result. Information on a paper roll.

## Slide 14: Maritime Cloud – MSI promulgation
Geocast + Acknowledge = Quality Assurance
MSI provider
Radioservice Z
Satellite service X
???
Defective comm
Satellite service Y
Geocast result:
11 vessels in region
10 acknowledge
1 missing (identity)
Region of relevance
Notes: This is how the situation could look if maritime safety information was promulgated using communication means with geocasting capabilities and acknowledgement of reception.
There would be quality assurance and malfunctioning equipment could be identified.

## Slide 15: Maritime Cloud – MSI promulgation
Geocast + Acknowledge = Quality Assurance
MSI provider
Radioservice Z
Satellit service X
???
Defekt comm
Satellit service Y
Geocast result:
11 vessels in region
10 acknowledge
1 missing (identity)
Region of relevance
Notes: Having communication means with more bandwidth would allow to send more data, for example geospatial information that can be presented directly on the navigational display.

## Slide 16: Highlights
e-navigation as an infrastructure and services as “apps”
Services will be able to evolve dynamically and can be provided by all maritime stakeholders, including commercial
Builds on existing proven technology i.e. cost effective
Security solution is proven and used today in e.g. the financial sector
Identity allows data sharing policies to be enforced
Facilitates seamless transfer from existing to new communication means
Availability and scalability addressed through distribution in a peer-to-peer architecture
Testbeds will early on be able to utilize the Maritime Cloud as a communication infrastructure to evaluate potential e-navigation solutions, and to evolve and mature the infrastructure itself
Has been submitted to the IMO e-navigation process as a proposed infrastructure that will support e-navigation in the short and the long run
Notes: So to summarize some of the consequences and highlights of the Maritime Cloud
It will support the notion of e-navigation as an infrastructure, and services seen as “apps”
Services will be able to evolve dynamically and can be provided by all maritime stakeholders, including commercial
It builds on existing proven technology therefore it can be cost effective
The security solution is proven and used today in for example the financial sector
Having identities that can be authenticated allow for data sharing policies to be enforced
It facilitates seamless transfer from existing to new communication means
Availability and scalability is addressed by a peer-to-peer architecture
Testbeds will early on be able to utilize the Maritime Cloud as a communication infrastructure to evaluate potential e-navigation solutions, and to evolve and mature the infrastructure itself
Finally, the concept has been submitted to the IMO e-navigation process as a proposed infrastructure that will support e-navigation in the short and the long run

## Slide 17: Status and the way forward
The infrastructure is currently being progressed in the ACCSEAS project where the Maritime Cloud will serve as the testbed infrastructure
Agile approach in which the the concept is continuously demonstrated and evaluated in practice
Conceptual and practical work progresses in parallel
Source code is open source for evaluation and collaboration http://maritime-cloud.net/
Political aspects to be investigated
  Possible governance structures
  Legal, cost and operational issues
Notes: So lastly the status and the way forward
The infrastructure is currently being progressed in the ACCSEAS project where the Maritime Cloud will serve as the testbed infrastructure.
We try to take an agile approach in which the the concept is continuously demonstrated and evaluated in practice
That means that conceptual and practical work is progressed in parallel.
All the source code developed will be available as open source for evaluation and collaboration, and will be available online.
A different track that has to be progressed is the political aspects. That is possible governance structures, and legal, cost and operational issues.
Important to note that because of the distributed architecture of the cloud, it will be able to accommodate many different governance structures.

## Slide 18: Thank you!
Contact information
Email
  obo@dma.dk
Website
  http://maritime-cloud.net/
Google group
  https://groups.google.com/d/forum/dma-enav