## Slide 1
Ship traffic management route exchange; acceptance in Korea and Sweden:
a cross cultural study
Thomas Porathe1, Ole Borup2, Jung Sik Jeong3, Jin Hyoung Park4, David Andersen Camre2, Anders Brödje5 1 Norwegian University of Science and Technology, 2 Danish Maritime Authority, 3 Mokpo National Maritime University, 4 Korea Research Institute of Ships and Ocean Engineering, 3 Swedish Maritime Administration
Notes: <number>

## Slide 2
Route exchange taxonomy
Tactical
route exchange
(intentions)
10-90 min
Transponder
transmitted
(ACCSEAS)
Strategic
route exchange
Total voyage
sent to STCC
Ahead of time
(MONALISA)
Dynamic
predictors
3-12 min
Onboard
computation
Collision avoidance zone – no route negotiations, look-out-through-the-window
Notes: <number>

## Slide 3
Tactical
route exchange
(intentions)
10-90 min
Transponder
transmitted
(ACCSEAS)
Strategic
route exchange
Total voyage
sent to STCC
Ahead of time
(MONALISA)
Dynamic
predictors
3-12 min
Onboard
computation
Collision avoidance zone – no route negotiations, look-out-through-the-window
Tested in Sweden Sep. 2013
& Korea April 2014
Route exchange taxonomy
Notes: <number>

## Slide 4
Tactical
route exchange
(intentions)
10-90 min
Transponder
transmitted
(ACCSEAS)
Strategic
route exchange
Total voyage
sent to STCC
Ahead of time
(MONALISA)
Dynamic
predictors
3-12 min
Onboard
computation
Collision avoidance zone – no route negotiations, look-out-through-the-window
Tested in Germany
& Sweden Sep. 2014
Route exchange taxonomy
Notes: <number>

## Slide 5
The HMI prototype of voyage plan coordination used
WP 0
WP 1
WP 2
WP 3
Voyage plan coordination (integrated into the ECDIS)
Notes: <number>

## Slide 6
The HMI prototype of voyage plan coordination used
WP 0
WP 1
WP 2
WP 3
Add WP
Show STCC info
Show route info
Show leg info
Delete leg 2
Activate route
Send to STCC
Voyage plan coordination
Notes: <number>

## Slide 7
The HMI prototype of voyage plan coordination used
WP 0
WP 1
WP 2
WP 3
Voyage plan coordination
Route is pending (waiting for answer)
Notes: <number>

## Slide 8
The HMI prototype of voyage plan coordination used
WP 0
WP 1
WP 2
WP 3
Route is “recommended” (from STCC)
Voyage plan coordination
Notes: <number>

## Slide 9
The HMI prototype of voyage plan coordination used
WP 0
WP 1
WP 2
WP 3
Ship acknowledges (or not)
Voyage plan coordination
Reject
Accept
Notes: <number>

## Slide 10
The HMI prototype of voyage plan coordination used
WP 0
WP 1
WP 2
WP 3
A mutually agreed “green” route
Voyage plan coordination
Notes: <number>

## Slide 11
The HMI prototype of voyage plan coordination used
New route is “recommended” (from STCC)
Old route is “not recommended”
WP 0
WP 1
WP 2
WP 3
New WP 2
Voyage plan coordination
Notes: <number>

## Slide 12
The HMI prototype of voyage plan coordination used
WP14, ETA 13.25
WP14, ETA 12.58
Voyage plan coordination
“Safe haven” – time slot
Target speed
13.4 kn
(13.2 kn)
COG 175.4°
SOG 18.4 kn
Lat 59 ° 15.794 N
Long 17 ° 13.859 E
Wind 124° 6.2 m/s
ROT
Route: Skag - Muga
Target SOG: 18.5 kn
Course: 175°
Dist. 23.4 NM
0.5
° /min
STCC monitoring service
Turn Sb 1 hr. 12 min. to 178 deg. Meet Tarnland on port, side in 23 min.
Send
Notes: <number>

## Slide 13
The HMI prototype of voyage plan coordination used
WP14, ETA 13.25
WP14, ETA 12.58
Voyage plan coordination
Target speed
13.4 kn
(13.2 kn)
COG 175.4°
SOG 18.4 kn
Lat 59 ° 15.794 N
Long 17 ° 13.859 E
Wind 124° 6.2 m/s
ROT
Route: Skag - Muga
Target SOG: 18.5 kn
Course: 175°
Dist. 23.4 NM
0.5
° /min
STCC monitoring service
Turn Sb 1 hr. 12 min. to 178 deg. Meet Tarnland on port, side in 23 min.
Send
Maritime Messaging Service
Notes: <number>

## Slide 14
The HMI prototype of voyage plan coordination used
WP14, ETA 13.25
WP14, ETA 12.58
Voyage plan coordination
“Safe haven” – time slot
Target speed
13.9 kn
(13.2 kn)
COG 175.4°
SOG 18.4 kn
Lat 59 ° 15.794 N
Long 17 ° 13.859 E
Wind 124° 6.2 m/s
ROT
Route: Skag - Muga
Target SOG: 18.5 kn
Course: 175°
Dist. 23.4 NM
0.5
° /min
STCC monitoring service
Turn Sb 1 hr. 12 min. to 178 deg. Meet Tarnland on port, side in 23 min.
Send
Notes: <number>

## Slide 15
The HMI prototype of voyage plan coordination used
WP14, ETA 13.25
WP14, ETA 12.58
Voyage plan coordination
“Safe haven” – time slot
Target speed
14.6 kn
(13.2 kn)
COG 175.4°
SOG 18.4 kn
Lat 59 ° 15.794 N
Long 17 ° 13.859 E
Wind 124° 6.2 m/s
ROT
Route: Skag - Muga
Target SOG: 18.5 kn
Course: 175°
Dist. 23.4 NM
0.5
° /min
STCC monitoring service
Turn Sb 1 hr. 12 min. to 178 deg. Meet Tarnland on port, side in 23 min.
Send
Notes: <number>

## Slide 16
Two studies comparing “professional acceptance”
STUDY 1 May 2013
Simulator study
(total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
Notes: <number>

## Slide 17
Two studies comparing “professional acceptance”
STUDY 1 May 2013
Simulator study (total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
Experiment Set-up
Two stations: 1 full mission bridge simulator (ship) manned with one professional captain, and one 4th year cadet; one VTS station manned with a VTS operator
Two test sessions, one in May and one in September 2013
Total: 12 blocks with 4 scenarios in each. Participants: 12 captains, 11 cadets, and 5 VTS operators (25 male, 3 female, ages 27-66, mean 42, professional experience 0-40 yrs. mean 15,7 yrs.)
Notes: <number>

## Slide 18
Two studies comparing “professional acceptance”
STUDY 1 May 2013
Simulator study (total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
Notes: <number>

## Slide 19
Two studies comparing “professional acceptance”
STUDY 1 SWEDEN May 2013
Simulator study (total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
STUDY 2 KOREA April 2014
Ship board (no control of own ship)
Chalmers University of Technology, Danish Maritime Authority,
Korea Maritime and Ocean University, Korea Research Institute of Ships and Ocean Engineering, Mokpo National Maritime University, Swedish Maritime Administration
18 cadets and experienced bridge officers
Notes: <number>

## Slide 20
STUDY 2 KOREA April 2014
Ship board (no control of own ship)
Chalmers University of Technology, Danish Maritime Authority,
Korea Maritime and Ocean University, Korea Research Institute of Ships and Ocean Engineering, Mokpo National Maritime University, Swedish Maritime Administration
18 cadets and experienced bridge officers
Two studies comparing “professional acceptance”
STUDY 1 SWEDEN May 2013
Simulator study (total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
Experiment Set-up
Two ships: EPD manned with one professional bridge officer, or one 4th year cadet; one VTS station manned with a VTS operator
One test session in April 2014
Total: 12 blocks with 4 scenarios in each. Participants: 9 bridge officers, 9 cadets, (12 male, 7 female, ages 20-51, mean cadets 21, professionals 38, professional experience 2-16 yrs. mean 11,3 yrs.)
Notes: <number>

## Slide 21
Two studies comparing “professional acceptance”
STUDY 1 SWEDEN May 2013
Simulator study (total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
STUDY 2 KOREA April 2014
Ship board (no control of own ship)
Mokpo National Maritime University, Korea Research Institute of Ships and Ocean Engineering, Korea Maritime and Ocean University, DMA, Chalmers, SMA
18 cadets and experienced bridge officers
Experiment Set-up
Two ships: EPD manned with one professional bridge officer, or one 4th year cadet; one VTS station manned with a VTS operator
One test session in April 2014
Total: 12 blocks with 4 scenarios in each. Participants: 9 bridge officers, 9 cadets, (12 male, 7 female, ages 20-51, mean cadets 21, professionals 38, professional experience 2-16 yrs. mean 11,3 yrs.)
Notes: <number>

## Slide 22
STUDY 2 KOREA April 2014
Ship board (no control of own ship)
Chalmers University of Technology, Danish Maritime Authority,
Korea Maritime and Ocean University, Korea Research Institute of Ships and Ocean Engineering, Mokpo National Maritime University, Swedish Maritime Administration
18 cadets and experienced bridge officers
Two studies comparing “professional acceptance”
STUDY 1 SWEDEN May 2013
Simulator study (total control of own ship)
Chalmers University of Technology,
Department of Shipping and Marine Technology
28 cadets, experienced bridge officers and VTS operators
Experiment Set-up
Two ships: EPD manned with one professional bridge officer, or one 4th year cadet; one VTS station manned with a VTS operator
One test session in April 2014
Total: 12 blocks with 4 scenarios in each. Participants: 9 bridge officers, 9 cadets, (12 male, 7 female, ages 20-51, mean cadets 21, professionals 38, professional experience 2-16 yrs. mean 11,3 yrs.)
Notes: <number>

## Slide 23
Notes: <number>

## Slide 24
Technical setup of the experiment
T/S Sae Nuri
T/S Hanbada
Notes: <number>

## Slide 25
Technical setup of the experiment
“The Maritime Cloud”
Notes: <number>

## Slide 26
RESEARCH OBJECTIVE
Familiarize participants with the route exchange idea enough so that they will be able to get an opinion on their “professional acceptance”.
Collect qualitative data on the concept, procedure change, functions and concrete HMA details
Notes: <number>

## Slide 27
METHOD
Usability Test (qualitative, moderated, talk-aloud video taped protocol)
Research questions:
Questionnaire: “What is your opinion about the tested route exchange concept?” and “Do you think a similar route exchange concept will become reality in the future?”
Conceptual level: Acceptance; unintended consequences of change
Procedural level: Changes, workload, manning
Functional and HMI levels: Detailed prototype improvements
Notes: <number>

## Slide 28
SCENARIOS
1. Send a route to STCC and agree
2. Change route under way initiated by ship
3. Change route under way initiated by shore
Notes: <number>

## Slide 29
Notes: <number>

## Slide 30
Notes: <number>

## Slide 31
Notes: <number>

## Slide 32
Notes: <number>

## Slide 33
Notes: <number>

## Slide 34
Notes: <number>

## Slide 35
Notes: <number>

## Slide 36
The “Safe haven”
Notes: <number>

## Slide 37
Close proximity warning
Notes: <number>

## Slide 38
Sweden
(n=18)
Korea
(n=19)
Questionnaire on “acceptance”
Notes: <number>

## Slide 39
Questionnaire on “acceptance”
Sweden
(n = 18)
Korea
(n = 19)
Notes: <number>