## Slide 1: 2nd Collaborated Test for e-Navigation Solutions in Korean Waters
Korea Research Institute of Ships & Ocean Engineering
Jin Hyoung PARK, Ph.D.
13th OCT. 2014, ITS World Congress, ENAV15, IALA

## Slide 2: Particulars of the test
2014. 9. 29. 09:00~22:30
SeaStarCruise: 14,000 tons, Mokpo  Jeju
Weather: cloudy, 5 miles of sight, 7 m/s of wind
Organization
  Attended: MOF, KRISO, ETRI, KR, KST, KIMFT, KMOU, MMU
  Supported: DMA (EPD systems)
ENAV15, IALA

## Slide 3: Test Systems
Messaging Server
EPD_Shore
Maritime Cloud
Shore
(KRISO)
IRIDIUM
KRISO_MSI
EPD_SHIP
ENAV15, IALA

## Slide 4: Test Scenarios
Route planning
  Route planning by using KRISO_MSI and EPD
  Sending the planned route
Monitoring ship status
  Sending ship status information on inclination, fire, flooding, engine failure to shore
  Sending S.O.S. to shore if necessary
Sending MSI to a ship
  Sending MSI to “a” ship
  Route modification due to MSI
  Warning from the shore side in case of an excessive deviation from the planned route
ENAV15, IALA

## Slide 5
ENAV15, IALA

## Slide 6: Lessens learned (1/2)
Test route
  Many chances of Encountering
    6 commercial ships
      Min. CPA: 0.3 miles
      3 times of deviation for C.A.
    17 fishery vessels
      Min. CPA: 0.2 miles.
      13 times of deviation for C.A.
  About 80% of head-on situation
  Many fishing nets and buoys
Acceptance level
  Cadets: full acceptance
  Captain & navigator: acceptable but no compelling need to use the systems in the real navigation
ENAV15, IALA

## Slide 7: Lessens learned (2/2)
Suggested way of application to the real world
  Fishery vessels: referring to the planned routes
  Commercial ships: more tolerances in “Safe Haven”
Hazards identified
  Potential negligence in watch-keeping due to communication (or negotiation)
  Restrictions on movement of navigator leading a drowsiness
  Errors in communication between ship and shore due to unsufficient training
  Excessive errors in PNT positioning information possibly leading to a hazardous situation in narrow waters
“Exemplary” application of a checklist for HCD
ENAV15, IALA

## Slide 8: Global Test Bed for e-Navigation (1/2)
Why “a global test bed” for e-Navigation?
  Inherent globality of Navigation
  Enhancement of berth-to-berth navigation and related services
  Supporting engineering process: validation & verification
  Tackling the technical challenges: CMDS, HCD, SQA&M, and harmonization
  Sharing the results globally
  Diversities in navigational environment
    Crew, traffic condition, weather, authority
  Scale effect
    “Proof of concept” at the global scale
    Effect/impact of new systems/services
ENAV15, IALA

## Slide 9: Global Test Bed for e-Navigation (2/2)
Components
  Components of regional test bed
  Interface linking regional test beds
Types
  Loosely-connected
    Partial inclusion of components of other test beds
  Tightly-connected
    Linking every components of each other’s
    Sharing test environments
ENAV15, IALA

## Slide 10: Thank you! jin.h.park@kriso.re.kr