## Slide 1: R-Mode for resilient PNT
Michael Hoppe, Jan Hendrik Oltmann, Stefan Bober, WSV
Dr. Gregory Johnson, Dr. Peter Swaszek, Alion Science a& Research
Juergen Alberding, Alberding GmbH

## Slide 2: Outline
    The need for terrestrial Backup
    The R-Mode Idea
Feasibiliy Study within ACCSEAS
  R-Mode using MF DGNSS Transmissions
  R-Mode using AIS Transmissions
  Combinations MF/AIS/eLoran
Test Beds
Conclusions

## Slide 3: The need for terrestrial Backup
Resilient PNT is a core element of e-Navigation and needs to meet maritime requirements for accuracy, integrity, availability and continuity
GNSS are vulnerable; development of a backup PNT system is recommended option
For e-Navigation (2018-2020 timeframe), IMO says:
  “.. there is a need to provide an internationally agreed alternative system for complementing the existing satellite PNT-services to support e-Navigation“

## Slide 4: Ship traffic density in the North Sea Region
ACCSEAS Baseline and Priorities Report

## Slide 5: The R-Mode Idea
R-Mode (Ranging Mode) is the transmission of accurate synchronized timing signals from existing terrestrial maritime radio infrastructure
Use of terrestrial radio links which are standardized and already globally distributed for maritime usage
    MF: IALA Radiobeacon Service (DGNSS)
    VHF: AIS-shore based service
Germany has contracted for a R-Mode Feasibility Study within EU-Project ACCSEAS for North Sea Region

## Slide 6
R-Mode using MF DGNSS Transmissions
  - Quick review of results -

## Slide 7: MF R-Mode range accuracy
Add CW ranging signal and occasional use of known RTCM message
  Range off of the phase estimate of the CW
  Use beat frequencies and bit transitions for ambiguity resolution
Notes: There are several important points to remember for MF DGNSS ranging:
Ranging using carrier phase requires the resolution of cycle ambiguity, the fact that the phase repeats every wavelength of the signal (this is approximately 1 km for MF DGNSS signals). Further, this cycle resolution is made more difficult for MSK since there is random data on the signal; hence, [3] recommended adding CW modulation to the transmission. CW allows for several ambiguity resolution approaches:
  Initializing the receiver at a fixed location and “counting” cycles as the platform moves.
  Using time synchronized, multiple frequency signals and solving for a position that simultaneously satisfies all of the ambiguity equations with integer solutions. This was accomplished in the Omega system by using different frequencies from spatially separated transmitters.
A second point is that this performance expression is the best possible (as predicted by a Cramer-Rao bound for the additive Gaussian noise model); actual performance will be somewhat worse.
A third point is that the propagation of an MF transmission is delayed according to the characteristics of the ground over which it is traveling. These additional secondary factors (ASFs) must be taken into account for positioning applications. While computer modelling tools can “predict” ASFs using databases of ground conductivity and topography, the quality of the prediction is typically insufficient for the desired positioning accuracy [4, 5]; the tools also do not describe the time varying nature of the ASFs. The standard solution involves surveying the area of interest to account for spatial effects based upon topography and ground conductivity and establishing monitor sites (with appropriate communications links) to provide temporal corrections to account for the time-variance in the conductivity.
Finally, MF transmissions can suffer from multipath interference due to signal reflections off of the ionosphere; this is referred to as sky wave interference. This effect is most pronounced at night. While pulsed signals (such as Loran) can mitigate this effect, continuous transmission (as in MF) will always suffer from it.

## Slide 8: DGNSS Geometry (HDOP)
MF sites with >7dB SNR and <500 km
Notes: SNR from Alion coverage software
Noise from ITU noise models
Skywave estimates from LFMF software using CCIR noise model

## Slide 9: MF R-Mode Position Accuracy
Day
Night
Signal strength predicted from Alion coverage software
Noise from ITU noise models
Sky wave estimates from LFMF software using CCIR noise model

## Slide 10
R-Mode using AIS-Transmissions
  - Quick review of results -

## Slide 11: AIS R-Mode range accuracy
Use existing signal with additional transmissions (# 4, 20, and 8, or 17)
  Range off of the bit edges
  Ambiguity resolution based on UTC clock synch
Notes: There are several important points to remember for AIS ranging:
On its own, the time of a bit transition has an ambiguity of one symbol period, 26.67 msec or, in range, 31 km. Given that the propagation range for AIS for ranging is expected to be out to 75-100 km, the bit transition time has limited ambiguity to resolve. For example, if the start of each AIS message is clearly aligned with a fraction of a UTC second (or some other system-wide reference), then this ambiguity is eliminated by knowledge of which bit edge it is within the message.
A second point is that this performance expression is the best possible (as predicted by a Cramer-Rao bound for the additive Gaussian noise model); actual performance will be somewhat worse.

## Slide 12: AIS R-Mode Geometry (HDOP)
AIS sites with signal strength>-117 dBm and <75 km

## Slide 13: AIS R-Mode Position Accuracy
Signal strength predicted using STK coverage software, based upon terrain (Terrain Integrated Rough Earth Model)
Noise from ITU noise maps

## Slide 14
Status of eLoran

## Slide 15: eLoran Geometry (HDOP)
Loran sites with signal strength
> 50dBμV
Ejde
Notes: HDOP for the five eLoran stations in region A1); Loran towers marked with black circles (Ejde is located to the NW just off the plot).

## Slide 16: eLoran Position Accuracy
All eLoran sites (5)
Reduced number of Loran sites (3)

## Slide 17: Combinations
All-in-view system
  MF and eLoran
    Region I
  MF and AIS
    Region II
  MF, AIS, and eLoran
    Region II

## Slide 18: Combined use of MF and eLoran
MF Day time accuracy
MF night time accuracy
@ Night and adding eLoarn (1)
@ Night and adding eLoran (2)
@ Night + eLoran (2) + MF (Ekofisk)

## Slide 19: Combined use of MF and AIS signals
MF Day
MF Night
AIS
MF-AIS Day
MF-AIS Night

## Slide 20
Combined use of MF, AIS and eLoran (1)

## Slide 21: Synergy of Combinations
System Combination | Performance level | Accuracy
MF DGNSS(day)-AIS-eLoran(1) | 1 | 0 –10m
MF DGNSS(day)-AIS | 1 | 
MF DGNSS(day)-eLoran(1) | 2 | 0 – 20m
MF DGNSS(night)-AIS-eLoran(1) | 2 | 
AIS-eLoran(1) | 2 | 
MF DGNSS(day) | 2 | 
MF DGNSS(night)-AIS | 3 | 0 – 50m
AIS | 3 | 
eLoran (5) | 3 | 
MF DGNSS(night)-eLoran(1) | 4 | 0 – 100m
MF DGNSS(night) | 4 | 

## Slide 22: MF R-Mode Test Bed in the Netherlands (Ijmuiden) within ACCSEAS
  Installation of R-Mode Testsite
  R-Mode Modulator and transmitter
  R-Mode receiver
Goals
  Proof of concept
  Assess of achievable performance in the field for timing and ranging

## Slide 23: Further possible future R-Mode test beds
R-Mode Testbed in the area of Amsterdam (NL)
R-Mode Testbed in the Baltic Sea (DK + D)
R-Mode Testbed in the German Bight (D)

## Slide 24: Conclusions
DGNSS R-Mode (MF and AIS) is a backup to GNSS that can meet the resilient PNT requirements of e-Navigation
To achieve widespread resilient PNT, the best solution is to use all signals available in a true all-in-view receiver.
It’s important to note that the need for a backup PNT is not uniform. The performance of a backup PNT system is most critical in the areas with the highest density of shipping traffic

## Slide 25
Michael Hoppe
German Federal Waterways and Shipping Administration Traffic Technologies Centre
Michael.Hoppe@wsv.bund.de
Questions ?