## Slide 1
Oct 2014
NAVDAT Test in China

## Slide 2
1. Introduction
NAVDAT is a new shore-based MF radio system, operating in the 500 kHz band for digital broadcasting of maritime safety and security related information and other service information.
NAVDAT can be used in improved shore-based services, e-navigation Risk Control Options (RCO 6).
NAVDAT will be an important system on the implementation of e-navigation strategy and the modernization of the GMDSS.

## Slide 3
1. Introduction
NAVDAT was induced as a new technology in recent years.
  In March 2012, a NAVDAT recommendation ITU-R M.2010 was released.
  At COMSAR 16 and NAV 58, documents about NAVDAT presented the main performances and some applications of the system (COMSAR 16/4/3, NAV 58/INF.17).

## Slide 4
1. Introduction
NAVDAT was considered as important technology in the modernized GMDSS and e-navigation.
  The document COMSAR 17/4 and NCSR 1/17 presented that NAVDAT might be one of new equipment, systems and technologies included in the modernized GMDSS.
  “Future communication systems could include VHF data (VDES) and NAVDAT, and be developed for internet based solutions, such as a maritime cloud, facilitating system wide information management solutions.” in document NCSR 1/9.
  By NAVDAT, “The same physical infrastructure can be reused to deliver higher bandwidth broadcast of an MSI information service using S-100 structured data.” in document NCSR 1/17.

## Slide 5
2. NAVDAT tests in China
Research and experiments of NAVDAT on system architecture, service content and technical standards have been carried out since 2013 in China.
NAVDAT test system was built in Donghai Navigation Safety Administration (DNSA).

## Slide 6
2. NAVDAT tests in China
The system is composed of the System of Information Source (SIS), System of Information and Management (SIM), NAVDAT Radio Station (NRS) (including modem, timing unit, transmitter, antenna tuner and MF transmitting antenna), NAVDAT shipborne terminal (including MF receive antenna, receiver, modem, display and control unit), GNSS receiver and Electronic Chart System.

## Slide 7
2. NAVDAT tests in China

## Slide 8
2. NAVDAT tests in China
The NAVDAT radio station was built in Shanghai Coast Radio Station.
Some equipment of NAVTEX, such as transmitter, antenna tuner and MF transmitting antenna, were reused.
The maximum power of existing transmitter was 5kW.
Test equipment layout
power indicator
Antenna
Spectrum

## Slide 9
2. NAVDAT tests in China

## Slide 10
3. Test contents of NAVDAT application
Test 1: Electronic Navigational chart (ENC) Update
  Updates and Corrections to ENC were made according to Notices to Mariners;
  The above update or correction patches to ENC were propagated by NAVDAT;
  The NAVDAT shipborne terminal received the patches and sent them to shipborne Electronic Chart System;
  The update or correction information could be displayed on electronic chart directly after manual confirmation;
  The test files were based on IHO S-57 standard nowadays, and S-101 the next generation ENC product specification will be tested in the future.

## Slide 11
3. Test contents of NAVDAT application
The original chart
Notice to Mariners
The chart was updated by NAVDAT
The pdf file of Notice to Mariners is 2,843 kB.
The update file of ENC is only 78 kB.

## Slide 12
3. Test contents of NAVDAT application
Test 2: Maritime safety related information broadcasting
  The Maritime safety related information including navigational warning, weather forecast, hydrographic note was broadcasted by NAVDAT.
  The above information contains both text and graphics, and XML format was adopted in the test .
  XML has come into common use for the interchange of data over the Internet.
  By this way, pictures and text could be displayed directly on personal computer.

## Slide 13
4. Discussion
Problems
  Lack of technical solutions for presenting maritime safety related information on navigational displays nowadays.
  Lack of suitable interfacing technique that could allow maritime safety and security related information to be presented on an electronic display to the mariner.
Solutions
  The most appropriate platform to present MSI may be either the INS or the ECDIS unit and optionally on another navigational display.
  Notices to Mariners, updates and corrections to ENCs and all nautical publications should be able to be received electronically with minimal delay by NAVDAT.

## Slide 14
4. Discussion
Application potential of NAVDAT
  Benefits from ENC Update
    NAVDAT allows more flexible ways of automated updating ENC, greatly reducing time and effort spent in manual correction and minimising the risk of human error.
    NAVDAT provide significant benefits to the mariner.
  Benefits from MSI related information combined text and graphics
    Easy to understand.
    Remove the risk of human error.

## Slide 15
4. Discussion
Limit of NAVDAT
  Although data rate of NAVDAT is higher than the NAVTEX, transfer time need to be considered for large file.
  500 kB File transfer time by NAVDAT:
Modulation | Data rate | Effective data rate | Transfer time
OFDM/4QAM | 12 kbps | 6 kbps | 83 seconds
OFDM/16QAM | 24 kbps | 12 kbps | 42 seconds
OFDM/64QAM | 36 kbps | 18 kbps | 28 seconds

## Slide 16
5. Conclusion
The NAVDAT test in China had made important progresses.
Much work remains on technical standard and on information exchange format.
China will continue to carry out NAVDAT test, and to provide better information services for ships.

## Slide 17
Thank you
Email: cdf123@139.com