## Slide 1
Harmonized Visual AtoN IoT
Jonas Lindberg, SABIK

## Slide 2
Who is this for?
What is the scope?
The proposed protocol
Conclusions
List of contents
Harmonized Visual AtoN IoT

## Slide 3
There are ongoing harmonization on e-Navigation but the visual AtoNs are mostly unconnected or in closed systems
The rapid technology development in IoT offers secure, low power and low cost solutions, but there is not a single ready standard to utilize
We believe the time is right to introduce a Harmonized IoT Protocol for Visual AtoNs
      Lantern data and health state
      Power system data and health state
      High Accuracy GNSS Position
        Collision detection
        Sea state estimation
        Big data analyses ... etc.
Harmonized protocol for what?
1997
2021

## Slide 4
DB
Database,
Presentation &
Asset Monitoring
Autethication & Message Relay
Monitoring
Mobile App
Monitoring Web App
Lighthouse
Buoy
A typical architecture can consist of:
Remote monitored visual AtoNs
Wireless Communication
    Client handler:
      Authentication
      Message handling
    Main server(s)/services
    User Interface
    The proposed standardization covers the portion inside the circle
System architecture
What is the scope?

## Slide 5
Asset Monitoring C
Asset Monitoring D
AtoN Manufacturer A
A typical architecture can consist of:
Remote monitored visual AtoNs
Wireless Communication
    Client handler:
      Authentication
      Message handling
    Main server(s)/services
    User Interface
    The proposed standardization covers the portion inside the circle
    If this can be standardized, the rest is ”easy” to integrate to most commonly used platforms
System architecture
What is the scope?
Standard AtoN IoT
Broker
AtoN Manufacturer B

## Slide 6
Harmonized Visual AtoN IoT Protocol
IoT infrastructure, MQTT
Security
Standardized Topics
Standardized coding of Topics

## Slide 7
IoT infrastructure
        MQTT, Message Queuing Telemetry Transport
        Lightweight and royalty free communication system
        Hardware agnostic, works on top of TCP/IP
        Commonly used > 1 billion connected devices
        Ready to use, integrated in many IoT hardware
        Takes care of:
        Device Communication (login, handshaking, etc)
        Data Transmission Ensures the efficient and reliable delivery of messages
        Broker Functionality It manages the routing and distribution of messages within the IoT system.
        Scalability and Flexibility
        MQTT is designed to be scalable and flexible. It supports lightweight clients and low-power devices, making it suitable for resource-constrained IoT environments.
MQTT Broker
Computer
Mobile Device
Sensor
Publish “23C”
Publish “23C”
Topic “temp”
Publish “23C”
Subscribe to ”temp”
Subscribe to ”temp”
Harmonized Visual AtoN IoT Protocol

## Slide 8
Security TLS 1.2 (Transport Layer Security)
        The current standard for online encryption and authentication
        Ready to use, already included in many new low powered IoT hardware
        Two way vs. One way communication
        For extremely critical AtoN infrastructure, or when remote commands are considered unnecessary, the implementation can be limited to only offer inbound messages from the remote AtoN
Harmonized Visual AtoN IoT Protocol

## Slide 9
Harmonized Visual AtoN IoT Protocol
Standardized Topics
        Topic ‘tele’
        Status, Uptime, Time, Alert Status, Location, Deviation, Beacon Status, Battery voltage, etc…
        Topic ’info’
        Protocol version, Type, System Information, Serial number, Product Identifier, Firmware version, etc...
        Topic ’cmd’
        Send, Reset, Light on Demand, Done, etc...
        Topic ’parameter’
        Ambient-light-level, distance-from-fix, fix-position, telemetry, low-voltage-disconnect, etc...

## Slide 10
Message structure in payload
        JSON, (JavaScript Object Notation)
        Human Readability: JSON is easy for humans to read and understand
        Data Interoperability: JSON is a widely adopted data interchange format
        Lightweight Format: JSON has a lightweight structure, meaning it requires less overhead compared to other complex data formats like XML
Harmonized Visual AtoN IoT Protocol

## Slide 11
Conclusion
MQTT is a lightweight publish/subscribe messaging protocol that enables efficient and frequent communication between devices in low-bandwidth, high-latency, or unreliable network environments. It supports SSL/TLS encryption enabling secure and authenticated communication. Used in conjunction with JSON, which is a platform-independent data format, it can be used with any programming language or platform.
Both MQTT and JSON are non-propriety and royalty free. Many open source platforms and libraries are available to support easy integration/adaptation.
IALA is invited to adopt this protocol and message structure as the standard IALA Visual AtoN Protocol (IVAP) to use so that members with a mixed network from various Industrial Members have the ability to monitor them in a single platform.
Harmonized Visual AtoN IoT Protocol