## Slide 1: Project ICING
Independent Critical Navigation
VDE-SAT Precision Time Service Tests
Hans.Christian.Haugli@spacenorway.no
Cato.Eliassen@kd.kongsberg.com

## Slide 2: Norwegian Consortium Pioneering VDE-SAT
Space Norway and Kongsberg Discovery - Seatex cooperation with ESA and NCA support
Norwegian Space Agency NorSat-2 demonstrations in the Arctic and elsewhere since 2017
  Weather broadcasting (Ice charts)
  New Search and Rescue Concept
  Mandatory harbour reporting
  AIS re-broadcasting at the North pole
  VDE-SAT Quality Monitoring System
Norwegian Space Agency NorSat-TD launched 2023
  Precision Time Service (subject of this presentation)
New Space Application Development Infrastructure Satellite to be launched 2025
Space Norway Test Service Infrastructure
  VDES payloads in space
  VDES router
  Quality monitoring nodes
  Selected applications
Kongsberg Discovery - Seatex
  VDES satellite payloads
  VDES ship terminals and shore infrastructure
Norwegian Space Agency NorSat-TD
(UTIAS/SFL)

## Slide 3: VDE-SAT Precision Time Service
GNSS jamming frequently experienced in the Arctic makes alternative navigation of increasing interest
Wanted to test if standard VDES signal from space could be used
ESA funded project under the NAVISP EL3 program to test a concept utilizing VDE-SAT VHF satellites to provide pseudo-range signals as a source of PNT
Consortium consisted of Space Norway (SPN) and Kongsberg Discovery, Seatex (KSX)
  SPN was Prime, Design Authority and owner of VDE-SAT payload on NorSat-TD
  KSX delivered VST x50 payload with updated FW, VDES 300 mobile station and VDES simulator software for timing estimation
Multiple received pseudo-ranges during single satellite pass used for location determination
VDES terminal to provide alternative PNT on the vessel
May also be used for integrity monitoring and anti-spoofing
VDE-SAT ranging has a potential for complementing other platforms used for alternative PNT such as Terrestrial R-mode.

## Slide 4: Test Configuration and Results
Test configuration
  VDES Link ID 29 waveform used (150 kHz bandwidth)
  Satellite position, speed and time sent in navigation message
  Remainder of payload static and optimized for correlation properties
  Timing accuracy of pseudo-ranges measured at one fixed location in Norway
Test results
  Concept worked quite well
  1 us measured timing accuracy
  1 km rms 2D position accuracy
  Small improvement using more than 20 satellite pseudo ranges

## Slide 5: Conclusions
Possible alternative PNT solution when GNSS is unavailable and at low cost
Existing VDES ship equipment
Satellite R-mode using existing waveforms may be used to determine ship location with better than 1 km accuracy off-shore
Improved accuracy in combination with VDE-TER R-mode
Other uses in include:
  Integrity monitoring
  Anti spoofing
  Position reporting based terminal derived positions, as more reliable than external GNSS
Invite IALA to consider need for VDE-SAT and VDE-TER Precision Time Service and requirement