## Slide 1: Simple qualitative assessment of risk “squart”
Stephen Bennett
Vice Dean; IALA World-Wide Academy

## Slide 2: Risk Assessment and Management
Chapter V Regulation 13.1 requires a Contracting Government to provide “such AtoN as the volume of traffic justifies and the degree of risk requires”
The determination of risk in each region, port or waterway is therefore an obligation on the Competent Authority of Coastal States
IALA has two proven risk management tools, IWRAP Mk2 (quantative) and PAWSA (qualitative)
However some developing CA may find the use of these tools difficult
SQUART, a simple qualitative tool, was developed to enable these States to meet their international obligations

## Slide 3: Definitions of Hazards and Risk
“Hazard” is an unwanted event or occurrence; a source of potential harm, or a situation with a potential for causing harm, in terms of damage to health, property, the environment, or other thing of value,; or a combination of these
“Risk” is the chance of injury or loss as defined as a measure of “probability or likelihood” and “severity or impact” of an adverse effect to health, property , the environment or other values

## Slide 4: Five Types of Hazard
A hazard is an unwanted event leading to a loss:
Natural: Storms; tides; tsunamis; solar flares
Economic: Recession; increased cost
Technical: Equipment failure; obsolescence
Human: Terrorism; war; poor training
Operational: Collision; grounding

## Slide 5: Five Step Risk Management Process
3
Specify Risk Control Options
4
5
Take Action to implement decisions
1
2
Identify and Prioritize Hazards
Assess the frequency and impact of each risk
Make a decision based on stakeholder feedback and ALARP options
Consult and report at each stage
Monitor results
Review regularly

## Slide 6: Review of Probability and Impact
Probability is the % chance of a hazard occurring based on:
  Maritime environmental studies and data (charts)
  Historical data and future trends
  Stakeholder feedback
  Traffic mix and density
  Human elements – e.g. crew competency (STCW)
  Categorized as “low”, “medium” or “high” ( 1, 2 or 3)
  The Consequence or impact of each type of unwanted event must be categorized as “minor”, moderate or severe (1, 2 or 3)
Risk = probability * consequence
Aim to reduce risks to As Low As is Reasonably Practicable (ALARP)
Reference: IALA Guideline 1018 on risk management

## Slide 7: Level of Risk Matrix
 |  | PROBABILITY |  | 
 |  | LOW (1) | MEDIUM (2) | HIGH (3)
IMPACT | SEVERE (3) | 3 | 6 | 9
 | MODERATE (2) | 2 | 4 | 6
 | MINOR (1) | 1 | 2 | 3
Risk = Probability * impact or consequence
1; 2 = acceptable: 3; 4 = caution: 6; 9 = unacceptable
ALARP

## Slide 8: SQUART Principles
Risk should be assessed on the worst possible scenario in a defined zone (region), port or waterway on any one day
An analysis of each Zone is conducted by the Competent Authority in consultation with stakeholders
Existing AtoN; hydrographic and meteorological data; traffic route, density and mix statistics and other factors are obtained from all available sources
Hazards are identified and prioritised
The frequency (probability) and impact of each risk is agreed
Control options are proposed for each risk

## Slide 9: Zones or Regions
Select zones with similar environmental conditions; volume and mix of traffic and potential hazards
Register of existing AtoN can be grouped by zone
Useful to base zone limits on published charts
Publish limits in Operational (navigational) plans
Zone 2
Zone 1
Zone 3
Zone 4

## Slide 10: SQUART Elements
MS Excel™ Workbook and MS Word ™ Instructions

## Slide 11: SQUART Contents
MS Excel Workbook:
Stakeholder worksheet
Statistical worksheet
Risk assessment and control option worksheet
Five page guidance document in MS Word
One Workbook per zone

## Slide 12: Stakeholder Worksheet
Stand-alone document
Completed by CA or AtoN service provider
Lists all those individuals, groups or organisations within each zone able to affect or be affected by a decision or activity related to AtoN service provision
Examples are provided, but list must be added to or amended as required
Reference IALA GL 1079 on User Consultation

## Slide 13: Statistical Data Sheet (Step 1 of Risk Management Process)
CA and selected stakeholders enter data obtained from all available sources in each section
hydrographic
Meteorological
Volume of traffic
Human factors
Economic factors
Simple Calculations made and automatically transferred to risk assessment worksheet
IALA “Facilitator” can assist if requested

## Slide 14: Risk Assessment and Control Options Steps 2 – 5 of Risk Management Process
Users at a risk forum enter a value of 1 to 3 for the probability and impact of each potential hazard based on experience or best estimates
Probability:
low = 1; medium = 2; high = 3
Impact:
minor = 1; moderate = 2; severe = 3
Control measures are then agreed
CA takes action to implement them

## Slide 15: SQUART Summary
A satisfactory understanding of the marine environment and maritime traffic patters is an essential element in the competency to be demonstrated by a Competent Authority
SQUART is a BASIC tool to achieve this understanding and generate risk control options
Considers the 5 types of hazard listed in IALA Guideline 1018
Based on objective user consultancy
First step in being able to use PAWSA and IWRAP Mk2

## Slide 16: Questions?
Contact: stephen.bennett@iala-aism.org