## Slide 1: Overview for stormy weather operation
Recommendation, and/or Instruction
  When severe weather is expected, the responsible VTS center, via appropriate means such as maritime traffic signals, recommends or instructs vessels to evacuate the area, and restricts or prohibits vessel entries.
  The VTS centers also recommends or instructs vessels to take appropriate measures in order to avoid dragging anchors and associated collisions.
  These measures are communicated well in advance of the anticipated severe weather conditions, thereby allowing vessels adequate time to respond appropriately.
  The VTS center alerts vessels within its operational area, which may be expanded in emergency situations, in order to prevent dragging anchors and associated collisions.
Advice, Warning and Information provided

## Slide 2: Overview for tsunami operation
Recommendation, and/or Instruction
  Immediately after a major tsunami is anticipated, the VTS center may restrict traffic within its responsible area, which may be expanded under emergency conditions.
  Such restrictions may include, but are not limited to, the following measures:
    Restriction of entry into the area
    Recommendation or instruction to evacuate the area
    Restriction of traffic routes
    Orders to relocate vessels within the area
  The VTS center may designate specific anchorage areas for vessels to prevent dragging anchor and associated collisions.

## Slide 3: Operational Flow for stormy weather（pre-storm-arrival）
Role | Operational Flow of VTS center
Anti-Stormy weather VTS operation | 
Receiving Severe Weather Information
Recommendation or Instruction:
Evacuation
Recommendation:
Anti-dragging-anchor preparation
Restriction or Prohibition:
Entering the VTS area

## Slide 4: Operational Flow for stormy weather（Under-stormy-condition）
Actor | Operational Flow
Vessel in the VTS area | 
VTS | 
Dragging anchor
Re-anchoring and or other appropriate action(s) (if necessary)
Monitoring Vessels in the service area
Detection of a dragging anchor
Reception of warning
Warning

## Slide 5: Operational Flow for Tsunami（Overview）
VTS | 
Vessels | 
・Evacuation to the safer area ・Waiting outside the port/bay
・Anti dragging anchor operation
・Listening to the information from the VTS center
Reception of information/recommendation/instruction
Monitoring the vessel traffic/ contact with vessels
Instruction on evacuation and prohibition of entering a port/ a bay
Navigational restriction/ prohibit of navigation
Designations of anchoring area and method
Restriction on Movement in the Port and Instructions to Leave