## Slide 1: DGPS Consultation
IALA Council #69, Rotterdam, 18th June 2019.
Martin Bransby – Head of Research and Development
General Lighthouse Authorities of the UK and Ireland

## Slide 2: DGPS is regional
sources: forobs.jrc.ec.europa.eu, IALA
Major shipping routes
DGPS radio beacons

## Slide 3: Coordinated service
It is clear (from SOLAS) that each maritime competent authority has the responsibility to determine the appropriate aids-to-navigation for their waters.
Marine radiobeacon DGPS is a coordinated service. Mariners access signals originating from different maritime authorities.
It makes sense for neighbouring/regional authorities to discuss their thoughts/plans on what to do next and why.

## Slide 4: Potential options
There are many options available, each with advantages and disadvantages.
They include:
Replace with a like-for-like service
Include alternative correction sources within the beacon network.
Upgrade to provide corrections for new GNSS constellations and/or new GNSS signals and frequencies.
Cease beacon operations and use different methods of providing corrections
But which option makes the most sense to follow and what do other administrations plan to do?

## Slide 5: External considerations
The world is also changing and developments in the following may affect what we opt to do next:
Global Navigation Satellite Systems (GNSS) development
Satellite Based Augmentation System (SBAS)
Receiver Autonomous Integrity Monitoring (RAIM)

## Slide 6: GNSS Developments
Marine beacon DGPS was developed in a time where GPS was used on its own as the only navigation satellite constellation available.
There will soon be 4 GNSS (GPS, GLONASS, Galileo and BeiDou) available, each providing civilian users with data on multiple frequencies.
It is believed that the majority of GNSS receivers used on vessels today are GPS single frequency; however, it is anticipated that mariners will equip with multi-GNSS receivers in the near future, when existing equipment needs replacing.
Multi-constellation, multi-frequency receivers will provide the user with greater accuracy (because of being able to calculate Ionospheric delay). They will also allow the receiver to use data from many more satellites (possibly 50+ compared to 12).
Q – Are differential corrections still required?
A – Integrity is still needed and not provided by the main GNSS… so maybe….

## Slide 7: SBAS
sources: www.gsa.europa.eu & forobs.jrc.ec.europa.eu
SBAS is a system developed to provide augmentation data for aviation users.
Regional systems exist around most of the northern hemisphere, with Australia developing a system in the southern hemisphere.
These systems can be used for maritime, although there are challenges to overcome.
Challenges include:
Recognition of a maritime user
Operational framework
Performance assessment
Standardisation of user equipment
Ship equipage

## Slide 8: SBAS challenges
Recognition of a maritime user
  On-going within Europe today for EGNOS, not clear for other SBAS. European Commission is formally considering a maritime service, which if approved, could lead to an operational service by 2022. IALA due to host public declaration of SBAS maritime performance.
Operational framework
  Through discussions with EMRF and various national administrations a framework is now agreed for EGNOS. This framework has been scoped at an international level so should be applicable worldwide.
Performance assessment
  The performance of EGNOS against maritime requirements is being assessed and routine updates provided to the IALA Radionavigation services WG of ENG. Again, the EGNOS service provider has been working hard to understand and map its services to a maritime environment.
Standardisation of user equipment
  Used on leisure vessels and within PPU today. Exists in most maritime receivers but not standardised. EC to support IEC test specifications which are expected to be complete by 2021/2022.
Ship equipage
  Equipage will not be mandatory but would be required before SBAS could be relied upon. Assume equipment available by 2022, but some time required for fleet take up.

## Slide 9: Receiver Autonomous Integrity Monitoring (RAIM)
RAIM uses additional satellites to test for faults to provide user level integrity.
Can operate in fault detect (FD) or fault detect and exclusion (FDE) mode.
It requires 5 or 6 satellites, depending on mode, but both require good GNSS satellite geometry.
RAIM has its own challenges:
Vague IMO requirement
Variable performance
Known performance issues
RAIM is evolving
Multi-Constellation, Multi-Frequency RAIM
Advanced RAIM
Maritime RAIM (M-RAIM)

## Slide 10: Receiver Autonomous Integrity Monitoring (RAIM)
Vague IMO requirement
  IMO GPS receiver performance requirements state a need for integrity and offer marine beacon and RAIM as examples. GLA understand RAIM is a requirement under European Marine Equipment Directive (2003+) but it’s not clear how this is replicated worldwide.
Variable performance
  Maritime standards don’t set the RAIM algorithm. There are many variants that can be used leading to inconsistent performance. More recent IEC test specifications are more defined in testing RAIM and it is anticipated that any new IEC work, such as the SBAS tests may be extended to update RAIM too.
Known performance issues
  The performance of single constellation RAIM is questionable. This is recognised by many including the IEC. Single constellation RAIM can lead to areas where there are simply not enough satellites, of sufficient geometry, to allow the approach to work.

## Slide 11: External events summary
SBAS and RAIM are both available and in use today – although neither is perfect.
SBAS could provide the mariner with integrity and accuracy improvement, similar to marine beacon DGPS. An EGNOS maritime service and IEC test standards are not expected until 2022/2023 and will need time for vessels to become equipped – perhaps achieved by 2025.
SBAS may not be recognised for maritime use in other areas and the approach has limitations at high latitude – so it’s not going to be the answer for all.
A GLA study showed that RAIM is generally available on approx. half of the vessels navigating in GLA waters. Algorithms in use today aren’t great and single constellation use can be questionable, but it can provide some integrity benefit.
Both SBAS and RAIM developments will require new receiver equipment and neither service is expected to be mandated.
Finally, both approaches are being developed further, although there is no clear timeline for either.

## Slide 12: Proposal
GLA propose that:
Council 69 hold an informal discussion on what you believe the future of IALA Beacon DGPS should be and why. It would be very helpful for all to talk over your views and expectations.
It is important to note that while overall trends may be captured, no personal or
national comments will be recorded – it is an informal, exploring discussion.
IALA Council invites ARM/ENG Committee to hold a workshop later in 2019 at which point national administrations are encouraged to provide experts with a considered position, with the aim to develop IALA Guidance on this matter.