## Slide 1: Use of Drones Rapporteur Report 9th IALA ENG Meeting
18 to 22 March, 2019
Jørgen ROYAL PETERSEN
Senior Engineer, Aids to Navigation
DMA - Safety of Navigation - National Waters

## Slide 2: IALA Conference 2018
Presentation at Conference:
  Building inspections
  Inspection of coastal protection
  Safety of personal/ working environment
  Fast, easy and cheap way to inspect
Future use:
  Verification of sectors in sector lights.
  Inspection of floating AtoNs and Offshore Beacon/ Lighthouses

## Slide 3: beyond the IALA Conference
Discussed opportunities with Danish National Drone Centre at University of Southern Denmark (SDU) and Lorenz Technology
Verification of sectors in Sector Lights is a demanding task…
Inspection of Floating AtoNs and offshore Beacon/ Lighthouses possible with known technology
  Visual status of top mark, colour and general condition.
  By Bluetooth link, battery voltage and status of lantern

## Slide 4: Known technology - Routine patrols

## Slide 6: Inspection schedule

## Slide 8: Video sequence from an inspection
Inspektion af bøjer v. Esbjerg Havn.mp4

## Slide 9: Drone for inspection and security
Wind stability up to 15m/s (wind gust)
- Max mean wind 8 – 12 m/s
Danish weather resistance
- Fly in showers and snow
Footprint 58 X 58 cm.
- In operation Ø1180
4 batteries
- App. 27 min. flight time per batteri
Mobile Powerbank - charging option
- Powerbank installed in the car for mobile charging
On board Lorenz AI-flight control
- Making the drone act on alarms
4G communication
- Communication link to the ServiceDesk (Hive 5.0)
VideoDrone X8L

## Slide 10: The Lorenz concept

## Slide 11: Challenges and trends
Operational time/ flying time – limited to 25 – 30 minutes (cold climate less than 5 – 15 minutes)
  Battery technology, safe energy source
  Fuel cells – operational time up to 70 minutes – costs seven times more expensive
Communication between operator and drone
  Legislation – today limited to flying only by visual line-of-sight
  Today 4G tomorrow 5G tele Network

## Slide 12: Underwater drone
For inspection of mooring or other underwater constructions/installations
Blueye Underwater Drone:
  Pressure rate: 150 meter
  Speed: 1.5 m/s (3 knots)
  Weight: 8.6 kg
  Battery: 96 Wh lithium ion smart battery
  Run-Time: 2 Hours
  Price: $ 9,878
https://www.blueyerobotics.com/pages/professional
Used by Norwegian Navy and Norwegian Coastal Administration

## Slide 13: Available information
More sharing – more knowledge in the ENG Committee!
If you have on-going trial on the use of Drones in your own Organisation/ Company don’t hesitate to contact me.
Or next time by your self contribute with relevant Drone information during the rapporteur session.

## Slide 14
Jørgen ROYAL PETERSEN, jrp@dma.dk