## Slide 1: Sustainability and Sector Lights
Competent Authority, Frank Hermann
ENG
AtoN
Engineering
and
Sustainability Committee

## Slide 2: Buying a sector light
colours, flashes, luminous intensity, sectors
unique
designed for a single station
fixed sectors
red: 2.12°
white: 0.81°
green: 1.84°
intensity and flash character
may be configured

## Slide 3: Buying 57 sector lights
r: 1.09°
w: 0.87°
g: 2.91°
r: 2.87°
w: 3.67°
g: 5.01°
r: 1.87°
w: 0.97°
g: 7.01°
r: 1.00°
w: 1.66°
g: 2.12°
r: 3.44°
w: 2.67°
g: 1.01°
r: 1.33°
w: 1.67°
g: 1.22°
r: 1.37°
w: 1.67°
g: 1.21°
r: 1.87°
w: 0.67°
g: 2.01°
r: 0.97°
w: 0.88°
g: 1.01°
r: 1.87°
w: 0.67°
g: 2.01°
buying 57 unique sector lights

## Slide 4: IALA Recommendation R0130 on Availabilty
  weakest category CAT3
  assume a light defect
  4 days to repair
  where is the manufacturer?
  solution proposed: for each station buy a complete sector light as spare part to replace a broken light within 4 days
  buy 2 x 57 = 114 sector lights

## Slide 5: 2 x 57 = 114 sector lights
r: 1.09°
w: 0.87°
g: 2.91°
r: 2.87°
w: 3.67°
g: 5.01°
r: 1.87°
w: 0.97°
g: 7.01°
r: 1.00°
w: 1.66°
g: 2.12°
r: 3.44°
w: 2.67°
g: 1.01°
r: 1.33°
w: 1.67°
g: 1.22°
r: 1.37°
w: 1.67°
g: 1.21°
r: 1.87°
w: 0.67°
g: 2.01°
r: 0.97°
w: 0.88°
g: 1.01°
r: 1.87°
w: 0.67°
g: 2.01°
57 additional lanterns as spare parts
NO !

## Slide 6: The Way to Sustainability, Requirement No. 1
Each sector must be adjustable by the owner.
Each sector must be adjustable at position.
Buy two sector lights as spare parts for 57 stations and configure them when necessary.
All work will be done by the operating company or competent authority.

## Slide 7: 'A sector light desaster'
  untighten a sector light
  means new alignment and commisioning
  causes immens efforts
  costs of new alignment and commisioning
    are left to administration
    may exceed costs of a new light by factors

## Slide 8: Example for a 'sector light desaster'
water
condensation, dirt
water in the optical cabinet
corrosion on lamp changer
could not dry the cabinet or clean the optical surfaces
look for an alternative light for temporary use
replace old sector light
install temporary light - comissioning
repare old sector light
reinstall repared old light - comissioning

## Slide 9: The Way to Sustainability, Requirement No. 2
Each lens surface and the optical cabinet should be accessible for cleaning and drying without changing the sectors (IALA GL 1041 13.3)

## Slide 10: Expected life time of a lights components
component | material | Expected life time
lens | glas | > 60 years
 | PMMA | ~ 30 years (avoid mechanical abrasion)
mirrors | glas (total reflexion) | > 60 years
 | silver, aluminium, dielectric | ~ 10 years when dry
filters | glas (absorption) | > 30 years
 | PMMA | > 10 years for low intensity lights
 | plastic film | ~ 5 years
mechanics | steel, aluminium | > 60 years
 | plastic | ~ 10 years
comparable objects |  | Expected life time
 | street illumination | > 30 years
 | a typical building | > 60 years

## Slide 11: The Way to Sustainability, Requirement No. 3
The electronic components have significantly lower expected life time than all other components.
All electronics should be reparable or replacable at position without causing a 'sector light desaster'.
  that means without changing a sector
  including replacing the LED

## Slide 12: Concept of LED modules for sector lights
replacable LED modules
a single projector for each colour
long life lantern (> 30 years)
replace LED and electronics periodically
replacable LED-modules

## Slide 13: The Way to Sustainability, Requirement No. 4
What about spare parts of a 20 year old sector light?
Does the manufacturer still exist?
open electronical interface
open mechanical interface
open optical LED specification
Make LED modules and controlers compatible.
Reject trademarks, non-disclosure agreements and patents for mechanical and electronical interfaces.

## Slide 14: Omnidirectional Sectorlights
Drum lens with optical filter
Tested LED modules from different manufacturers to replace classical light sources in drum lenses
Poor results:
      low intensity
      false colour
      large angle of uncertainty

## Slide 15: Use of projectors for omnidirectional sectorlights?
14 different sectors
Luminous intensity ~ 100 000 cd
Replace with 36 x 10° projectors?
NO !

## Slide 16: The Way to Sustainabiltiy, Requirement No. 5
high luminous intensity
small vertical angle (< 5°)
large horizontal sector (≥ 45°)
Reinvent anamorphic optics
8 x 45° projectors

## Slide 17: Other types of lanterns
Leading light lanterns
Rotating optics
Projectors
Can be driven with the same LED-modules.

## Slide 18: The Way to Sustainabiltiy, Requirement No. 6
Reduce the diversity of light sources.
~ 54 different type of lamps in use
Leading lights, sector lights, rotating optics
?
Old fresnel lens: drum lens type or rotating

## Slide 19: The Way to Sustainability
Additional requirements ...
The old technology has been proven to be very sustainable:
      life time of steel buoys ~ 40 years or more ...
      life time of optics ~ 60 years or more ...
Retain existing sustainability!
Well planned maintenance from the beginning
      'maintenance free over lifetime' will not give sustainable products
      'is recycable' does not mean 'will be recylced'

## Slide 20
Waste
Initiative aiming for
  fair trade
  environment protection
'Use jute bags instead of plastic bags'
Started in the year 1978
What happened since then?
Friday for Future
Youth Strike 4 Climate

## Slide 21: Sustainability and Sector Lights
Germany is going to update its AtoN lights
open competitive bidding
starts 2020
sustainable design specification
www.evergabe-online.de
Federal German Waterways and Shipping Administration, Wilhelmshaven, Frank Hermann