## Slide 1: Report from rapporteur regarding Risk Management and Risk Models Monitoring item M1 Jakob Bang Danish Maritime Authority
IALA ANM 21
October 2013

## Slide 2
Removal of Drogden lighthouse
Use of simulation and IWRAP

## Slide 3
Location of Drogden Channel

## Slide 4
Present conditions
Dredged channel
40.000 ships per year,
300 m width
8 m depth
Offshore lighthouse in the Southern part

## Slide 6
AIS tracks

## Slide 7: Virtual AIS-AtoN

## Slide 8
IALA Guideline No 1058
Initial analyses between FORCE and DMA:
Identifying the objectives of the project, geographic boundaries etc
Confirming the operational requirements, vessel types, traffic density, met-ocean conditions
Define the scope of feasible marking

## Slide 14
IWRAP model

## Slide 15
IWRAP results
 | Years between incidents Default causation |  |  |  | Years between incidents 0.5*default causation*) |  | 
Collision type | Drogden | Light house removed | Change |  | Drogden | Light house removed | Change
Overtaking | 123 | 119 | 4% |  | 123 | 237 | -48%
HeadOn | 77 | 72 | 7% |  | 77 | 144 | -46%
Crossing | 7348 | 34014 | -78% |  | 7348 | 34014 | -78%
Merging | 286 | 462 | -38% |  | 286 | 925 | -69%
Bend | 70 | 88 | -21% |  | 70 | 176 | -60%
Total Collisions | 26 | 28 | -8% |  | 26 | 56 | -54%
IWRAP Results
The model for the current situation has been processed using IWRAPs default causation factors. It could be argued that the causation factors should be lowered in the new situation where the navigator does not have to think about the turn around the light house.
In the results below we have made the calculations with the default causation factors and causation factors that are half of the defaults. The overall result is that the number of expected collisions decrease from one every 26 years to perhaps one every 56 years.
This value depends on how much the removal of the light house frees up the navigator mind. In any case the result of removing the light house does not lead to a situation worse than today.
*) Means that the navigators will be twice as alert as today.

## Slide 16
Conclusions and status
Remove Drogden Lighthouse
New surveys in the area are completed
We await economic calculations about the methods to remove Drogden Lighthouse
We expect to remove Drogden Lighthouse in 2014

## Slide 17
IWRAP workshop in Aalesund, Norway
Danish and Norwegian maritime authorities
A number of IWRAP models were conducted and the results and technical features were discussed
Our common challenges in Arctic waters were considered

## Slide 18
IALA WWA ACADEMY TRAINING SEMINAR ON RISK MANAGEMENT:
PAWSA, IWRAP Mk2 & SIMULATION
11 November – 15 November 2013
MADRID, SPAIN

## Slide 19
The sleeping helmsman