## Slide 1
17 April, 2012
Republic of Korea
Ministry of Land, Transport and Maritime Affairs
EEP18/8/17
Notes: <number>

## Slide 2: GyeongIn-Ara Waterway
Notes: <number>
<number>

## Slide 3: GyeongIn-Ara Waterway
floodgate
Traffic signal lamp
Notes: <number>
<number>

## Slide 4: GyeongIn-Ara Waterway
Steel Buoys
Notes: <number>
<number>

## Slide 5: GyeongIn-Ara Waterway
Plastic Buoys
Notes: <number>
<number>

## Slide 6: Plastic Buoy
Plastic Buoy (PB-15)
Material : PE (Polyethylene)
Rotationall moulded UV-stabillised virgin PE float section
Foam Filling : Expanded Polyurethane Foam
Notes: <number>
<number>

## Slide 7: Plastic Buoy
Plastic Buoy (PB-15)
Diameter : 1.5m
Height of Buoy : 2.6m
Weight : 312.3 kg
Buoy body thickness : 12mm
Maximum current : 4Knots
Maximum Water depth : 15m
Mooring : Elastic mooring
Notes: <number>
<number>

## Slide 8: Plastic Buoy
Plastic Buoy Rotational Molding
First Stage
Loading resin in the mold
Second Stage
Heating and fusion of resin
Third Stage
Cooling prior to unloading mold
Notes: <number>
<number>

## Slide 9: Plastic Buoy
Installation of Plastic Buoys
Notes: <number>
<number>

## Slide 10: Plastic Buoy
Variation of surface color
Notes: <number>
<number>

## Slide 11
Jin-Gee Jeon
Maritime Traffic Facilities Division Office
of Logsitics and Maritime Affairs
Ministry of Land, Transport and Maritime Affairs
47, Gwanmun-ro, Gwacheon-City, Gyeonggi-do,
Korea 427-712
Tel : +82-2-2110-6386
Fax : +82-2-504-4076
e-mail : joengingee@korea.kr
Thank you very much
for your attention!
Notes: <number>