## Slide 1: Calculation of Light
Frank Hermann, German Waterways and Shipping Administration
Illumination
Of
Structures
Notes: <number>
Variable message signs can be used for waterways with a strong tide.
They can show the water level, bridge clearance or stream information.
Other applications are signalling a temporary shut of a waterway or information about traffic regulation.

## Slide 2: Formula
taken from: ‚Grundlagen der Lichttechnik‘ Dietrich Gall – (fundamentals of light technology)
Notes: <number>
Example1
Maritime waterway
It hows the water level and indicates high and low tide.
It is a tricky combination of rotating tubes with fluorescent lamps.

## Slide 3: Light is a huge market
Notes: <number>

## Slide 4: Market
Illumination
Signal Lights
Marine Signal Lights
Notes: <number>

## Slide 5: Tools exist for Computer Calculation
  Ensure the correct illumination level
  Avoid glare
  Find suitable luminaires
  Find the correct positions and numbers of luminaires
  Visualize a scenery for optimization
  NOT FOR Signal Lights
Notes: <number>

## Slide 6: Calculation Procedure
Geometrical Data
(road, floor, building)
Surface Data
(colour, glossiness, texture)
Luminaire data
(intensity distribution, colour)
Luminaire number and position
Calculation
Illuminance E (lx)
Luminance L (cd/m²)
Uniformity of illumination
Colour
Visualization
Glare
Notes: <number>

## Slide 7: Example program: Dialux
  Freeware for MS Windows
  www.dial.de
  international luminaire catalogues (> 150 manufactureres)
  Endo-Japan, Megaman-Hongkong, Nikkon-Malaysia, PAK-China, Opple-China, Pierlite-Australia, Riegens-Denmark, Indal-Spain, Lival-Finland, Artemide-Italy, Thorn-UK, Saudi-Lightning-KoSA, ASTZ-Russia, Batpa-Ukraine, GreenRay-US, IPI-Portugal, ...
  Alternative European Product: Relux-Switzerland, www.relux.biz
  Various programs: Visual – US, www.visual-3d.com
  Synopsis Light Tools - US
Notes: <number>

## Slide 8: Dialux
  Scenery data
  Design with Dialux
  Import 2D-Data as DXF-File and extrude
  Import 3D-Data as 3DS-File
  Surface data
  Select with Dialux
  Luminaire data
  Import LDT-File (Luminaire Data File)
  Import extended Luminaire Data Files (UDT, SDT)
Notes: <number>

## Slide 9: Object Data
Notes: <number>

## Slide 10: Luminaire Data
Notes: <number>

## Slide 11: Results: Rendering
Notes: <number>

## Slide 12: Results: Illuminance (LUX isoline)
green
white
red
Notes: <number>

## Slide 13: Results: Illuminance (LUX charts)
green
white
red
Notes: <number>

## Slide 14: Results: Luminance (Candela/m² isoline)
green
white
red
Notes: <number>

## Slide 15: Results: Luminance (Candela/m² isoline)
green
white
red
Notes: <number>

## Slide 16: Maritime Building
Notes: <number>

## Slide 17: Caution
Light:
Luminous intensity IS
Candela
Illuminated area:
Luminance L
Candela/Metres²
Size A
Metres²
Notes: <number>

## Slide 18: Illuminated area as a rival light
From far distance:
Illuminated area appears as a spot
with intensity IR = A*L
and becomes a rival light
Notes: <number>

## Slide 19: Countermeasures
Calculate L and the illuminated area A and choose IS >> IR = L*A (e.g. I > 10*Is)
Separate the illuminated area from the top light (e.g. 5 arcminute for largest viewing distance)
Skip the light (for port entrance) The illumination should then correspond to IALA system: red and green.
Notes: <number>