## Slide 1
ZTI 1250
GPS based Timing Signal Generator for Maritime and Fluvial Traffic Lights
ZTI 1250 is designed to be easily integrated in most of already installed lights
ZTI 1250 makes Maritime and Fluvial Traffic Lights synchronized
ZTI 1250 manages automatically twilight switch on / switch off

## Slide 2
© ZTI March 2013
ZTI 1250
<number>
TOPIC
Why ZTI 1250 has been done for?
Example of use
Features
Specificities
ZTI 1250 Physical description
ZTI 1250 SYNAPSE software
Integration of ZTI 1250 with a LED Flasher SABIK
ZTI 1250 Starter kit

## Slide 3
© ZTI March 2013
ZTI 1250
<number>
Why ZTI 1250 has been done for?
Regarding port approach, sailors and boat drivers are sometimes mislead by unsynchronized maritime or fluvial traffic light and complain to Port Authority
The GPS technology allows now a perfect synchronization. However, a large part of the installed park of maritime and fluvial traffic lights have not this feature
ZTI 1250 has be designed to be installed in almost existing traffic lights
  To synchronize traffic lights
  To manage the traffic light (switch on / switch off)
  To signal any out of position of buoy or beacon
The CETMEF in France (Institute for Maritime and Inland Waterways from the French Agency for Ecology, Sustainable Development and Energy) uses now ZTI 1250 to manage traffic lights in several French ports that were problematic
ZTI 1250 gives full satisfaction to Port Authorities
Deployment of ZTI 1250 in France, for hundreds of alignment lighthouses, fairway buoys and port entry doors, is underway

## Slide 4
© ZTI March 2013
ZTI 1250
<number>
Example of use
La Rochelle, France
  Red and green lights are synchronized by ZTI 1250

## Slide 5
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 Features
GENERAL
  ZTI 1250 delivers GPS based Timing Signals for Maritime and Fluvial Traffic Lights
  ZTI 1250 delivers GPS location
  ZTI 1250 manages 2 functions selected among 4 ones and 1 GPS default alarm
TOP synchronization
  Pulse with frequency, duration and delay user configurable based on signal PPS (Pulse Per Second with ± 2.5 ns accuracy)
Time scheduler
  Automatic switch on / switch off, based on UTC solstices and equinoxes
Twilight switch
  Automatic switch on / switch off, based on GPS position and selected offset
Out of position
  Signal when the device gets away from an allowed radius around its defined position (GPS or specified)
System default
  Signal when a problem occurs : GPS antenna, satellites not in view…

## Slide 6
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 Features
Hardware Management interface
  RS232 interface (9600bps, without parity, 8 bits, 1 stop bit)
  Connector DB9 female
Software Management interface
  SYNAPSE software for MS Windows™
    Monitoring mode
    Programming mode
    Terminal mode (NMEA messages)
Output 2 selection
Output 1 selection
Output 2 selection

## Slide 7
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 Specificities
81.3 mm
66.0 mm
Extended environmental conditions
  Temperature: -40°C to +85°C
  Humidity: 5% to 95%, non condensing
PCB protected by varnish
Very low power consumption
  Operation mode: 312 mW
  Low power mode: 72 mW / 120 mW
Reduced size
  To fit in any device beacon, buoy, …
  Optimized shape for passing wires and for fastening
2 years warranty

## Slide 8
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 Physical description

## Slide 9
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Monitoring mode displays
  Date
  UTC Time
  GPS position
  Signal quality
  Output 1
    Function
    Information
  Output 2
    Function
    Information

## Slide 10
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Programming mode sets up
  TOP Synchronization
    Pulse duration
      2 to 500 ms
    Period
      60 to 480 s
    Delay (*)
      0 to 5 s
(*) Could be used for shift lightning

## Slide 11
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Programming mode sets up
  Time scheduler (*)
    UTC Winter solstice
    UTC Equinoxes
    UTC Summer solstice
(*) From the 3 UTC times, ZTI 1250 calculates the on and off switching time (linear extrapolation).
ZTI 1250 Module
/ Output #1
Hours of the winter solstice
Active
Inactive
ZTI 1250 Module
/ Output #1
Hours of the equinoxes
ZTI 1250 Module
/ Output #1
Hours of the summer solstice
Active
Inactive
Active
Inactive
Time of activation
Time of desactivation
Time of activation
Time of desactivation
Time of activation
Time of desactivation
Decrease or increase the activation duration

## Slide 12
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Programming mode sets up
  Twilight switch
    Twilights computed by ZTI 1250
    Time offset defined by
    the user ±5 hours

## Slide 13
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Programming mode sets up
  Out of position data
    Position is defined by GPS or by the user
    Allowed radius is defined by the user
    Real position is computed by ZTI 1250
    Signal output if out of position

## Slide 14
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Programming mode sets up
  Sleep delay is defined by the user between 0 to 30 s

## Slide 15
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 SYNAPSE software
Terminal mode displays
  NMEA messages when red micro-switch # 2 on the board is on

## Slide 16
© ZTI March 2013
ZTI 1250
<number>
Integration of ZTI 1250 with a LED Flasher SABIK™

## Slide 17
© ZTI March 2013
ZTI 1250
<number>
ZTI 1250 Starter kit
A starter kit is very useful tool
  For starting
  For training
  For programming modules
  For testing
Features
  Socket for ZTI 1250
  Choice of power supply
    220 V AC adapter
    3 to 40 DC input
  LED indicators
  Configuration switches
  Testing points

## Slide 18
1 boulevard d'Armor BP 20254 22302 Lannion Cedex FRANCE
Sales David Cohen +33 6 62 52 32 22 david.cohen@zti-telecom.com
www.zti-telecom.com