## Slide 1
Lantern Glazing – Glass or Acrylic

## Slide 4
Acrylic is much cheaper
  Glass Diamond Euro 928 (US$ 1,272)
  10mm Acrylic Diamond Euro 347 (US$ 476)
Acrylic is lighter and safer to handle
Acrylic is more tolerant of thermal movement within the glazing frame
Acrylic is more prone to scratching and abrasion

## Slide 5
Optical Performance
 | Glazing |  |  | Max Measurement Uncertainty (%) to 95% Confidence | 
 | 10mm Perspex % Transmission | 10mm Laminated Glass % Transmission | 10mm Solid Glass % Transmission |  | 
Run 1 | 95.25 | 92.25 | 86.49 | 3.7 | 
Run 2 | 96.11 | 89.23 | 86.36 | 3.7 | 
Run 3 | 95.98 | 89.21 | 86.77 | 3.7 | 
Average | 95.78 | 90.23 | 86.54 |  | 
STDEV | 0.46 | 1.75 | 0.21 |  | 
Total Uncertainty (%) 95% Confidence | 3.8 | 4.3 | 3.7 |  | 

## Slide 6
Acrylic
Specification

## Slide 7
Conclusions:
Acrylic is a suitable and cheaper alternative to glass for lantern glazing
Long term performance > 10 years has yet to be proven
< Half the price of glass
Significant safety improvements in handling
Acrylic is more tolerant to movement in service