## Slide 1: Traditional Revolving Optic Re-Engineered for Continued Operation without Mercury
IALA EEP Committee
21th Session, October 7 – 11, 2013
St. Germain en Laye, France
Jørgen ROYAL PETERSEN
Senior Engineer Aids to Navigation
Danish Maritime Authority (DMA)

## Slide 2: Overview
In 2008 The Danish Maritime Safety Administration (DaMSA), now Danish Maritime Authority (DMA), had thirteen (13) operational lighthouses with Mercury Bath System.
Spillages of Mercury at Nakkehoved Lighthouse caused by an earthquake in Sweden in December 2008 tense up the Authorities focus on use of Mercury at Danish Lighthouses.
Due to the environmental aspect in general and in agreement with the Danish Working Environmental Authority in 2009, it was decided to close down all Mercury Bath Systems over a five years period (before 2015).
A Nautical analysis has shown that 2 lighthouses with Mercury Bath System could be closed down. 11 lighthouses have further nautical importance - however some with reduced optical range – 18 NM

## Slide 3: A future without Mercury
In general two models are
selected to meet the nautical
requirements and maintain the light:
In general high intensity LED flashing lanterns with a range of approx. 18 NM. (The Mercury is after then removed and the lens table is locked in a suitable position)
At listed and historic lighthouses considerations should be taken for preserving the original revolving optic.

## Slide 4
1. Generation of Revolving Optic
Roller Carriage System for Large Revolving Optics
Revolving Optic systems designed before 1889 had to be turn around on a roller carriage.
The speed was slow and the flashes infrequent due to the friction in the system.
The low speed of the optic requires small narrow and ineffective optical panels to obtain a reasonably frequent repetition of the flash.

## Slide 5: Roller Carriage System for Revolving Optic
Pictures from Hanstholm Lighthouse (DK) and Nolsø Lighthouse (Faroe Island)

## Slide 6
2. Generation of Revolving Optic
Mercury Bath System for Large Revolving Optics
In 1889 the French Lighthouse Service designed the Mercury Bath System and the first system was operational in 1892.
The system was designed for large optics to be supported upon an iron carriage floating in mercury.

## Slide 7: Mercury Bath
Major advantaged of Mercury Bath System:
  The weight machine could be smaller and operate all the night on a few windings.
  The lens could be turn around more rapidly and it was possible to enlarge the area of the lens and still obtain a reasonably frequent repetition of the flash
  Greater area of the optic provides higher intensity with the same light source.

## Slide 8: Comparing size of optic for Roller Carriage System and Mercury Bath System

## Slide 9: Project ProMerc
Model 2: At listed and historic lighthouses considerations should be taken for
preserving the original revolving optic.
The aim of project ProMerc was to find a suitable technical solution which also takes into account the historical and heritage aspect .
Additional to the basically engineering work the aim of the project was therefore to find a solution avoiding significant changes of the original construction and preserve the authentically expression of the unique installation on an operational lighthouse.
In co-operation with The Technical University of Denmark (DTU) efforts was taken on design and re-engineering work to re-build the revolving system at Nakkehoved Lighthouse (a operational heritage listed lighthouse with a Lighthouse Museum in the dwelling).
At the end of 2012 a draft project was presented by DMA and this was approved by the Danish Agency for Culture.
In January 2013 the detailed design project was initiated and by the end of April 2013 the re-engineered system was put into operation.

## Slide 10: Nakkehoved Lighthouse
First Orders Catadioptric Fresnel Lens (focal distance 920 mm)
Weight of lens and support approx. 5 Tons
Optical range 20 NM

## Slide 11
Upper Bearing
Lower Bearing
Vertical Limitation Device
Circular Cast Iron Vessel
Circular Bath for Mercury
Support for Optic
Principle

## Slide 12
Upper Bearing
Lower Bearing with Vertical Limitation Device
Circular Cast Iron Vessel
Circular Bath for Mercury
Support for Optic
Original System
Re-Engineering:
The Bath
The lower Bearing

## Slide 13: Lower Bearing in position
Locknut
Shaft with thread
Conical Tap

## Slide 14: Technical pre-evaluation of the Project
Load at floor separation – the load is removed from three support pillars to a single point load in the centre of the floor
Evaluation of the floor separation beams – safety factor 9/2.5
Evaluation of the Vertical shaft – deflection and fracture – safety factor 17
Bearing calculation and lifetime assessment – 300/40 years
Evaluation of the new construction elements

## Slide 15: Removed Lower Bearing with housing

## Slide 16: Installation of Thrust Roller Bearing

## Slide 17: Adjustable bearing support

## Slide 20: Installation of Thrust Roller Bearing

## Slide 21: Installation of Thrust Roller Bearing

## Slide 22: Adjustable bearing support

## Slide 23: Removing Mercury Bath topped up with Kerosene to avoid evaporation of Mercury from the surface of floating vessel and bath.

## Slide 24: Economy and Business Case
New Lantern (Model 1) compared with a Re-Engineering (Model 2):
Equal cost for both solutions approx. DKK 150,000 ~ € 20,000
Cost of Prototype DKK 200,000 ~ € 27,000
Lifetime LED Lantern ~ 10 years
Lifetime Bearing ~ 40 years

## Slide 25: Experiences and Conclusion
Experiences:
The replacement of the new trust bearing and additional supports were carried out in one day - approx. 8 hours – therefore no needs to take the lighthouse out of operation.
During the initial test run and after 6 month no vibrations or atypical reactions are recognised in the pedestal or in the optic.
Energy consumption of the electrical drive has been reduced with 17 % compared to the Mercury Bath System.
Conclusion:
It can be concluded that the re-engineered Mercury Bath System works excellent - from the first day and after 6 month no changes are recognised.
The plan is – with respect to the original design and where it is possible – implementing the described design at historical and listed lighthouses in Denmark
As shown by the Business Case the Re-Engineering project is cost-effective and addition to this it’s caring about the Heritage and remain the beautiful swiping light.

## Slide 27: Recommendations
It is strongly recommended that Lighthouse Administrations and owner of lighthouses consider and prepare a close down plan for Mercury Bath Systems because there are an increasing international focus on use and handling of mercury due to the toxic influence on the nature and the human body.
Sooner or later the demands will also come from your National Authorities.
Lesson learned in Denmark is that the demands from the Authorities are comprehensive, time consuming and very expensive.

## Slide 28: Thank you very much for your attention jrp@dma.dk