## Slide 1
<<FeatureType>>
AtoN
+ name : Text
+ id : Text
+ code : Text
+ colour : Colour
+ colourpattern : ColourPattern
+ shape : Text
+ establishedDate : Date
+ surveyedDate : Date
+ daymark : dayMark
+ position : GM_Point
<<FeatureType>>
Fixed_AtoN
+ altitude : Real
<<InformationType>>
AdministratingAuthority
+ organization : Text
+ country : Nationality
+ telephone : Text
+ email : Text
<<FeatureType>>
AtoNAIS
+ mmsiNumber : Integer
+ calculatedRange : Real
+ aisRxTx : AISRxTx
+ elevation : Real
+ status : Text
+ name : Text
+ id : Text
+ code : Text
+ installedDate : Date
+ surveyedDate : Date
<<FeatureType>>
Racon
+ frequency : Real
+ power : Real
+ whistlingCycle : Text
+ name : Text
+ id : Text
+ code : Text
+ installedDate : Date
+ surveyedDate : Date
<<FeatureType>>
Beacon
+ islightfitted : Boolean
+ lightHeight : Real
<<FeatureType>>
LightHouse
+ lighthouseType : TypeOfLightHouse
+ height : Real
+ includelight : Light
+ lightHeight : Real
<<FeatureType>>
SectorLight
+ includelight : Light
+ lightHeight : Real
+ whiteSector : Angle
+ colouredSector : ColourSector
+ obsecuredSector : Angle
+ angleOfUncertainty : Angle
+ secondaryLight : Light
<<FeatureType>> Floating_AtoN
+ availabilityOfAtoN : PerformanceCriteria
+ elevation : Real
<<FeatureType>>
Buoy
+ islightfitted : Boolean
+ bouytype : BuoyType
+ buoyshape : BuoyShape
<<FeatureType>>
LightVessel
+ lightHeight : Real
GM_Point
+ point
<<InformationType>> dayMark
+ marktype: TypeOfMark
+ ialaRegion : IALARegion
+ islightfitted : Boolean
+ lightRhythm: RhythmofLight
<<FeatureType>>
LightFloat
+ height : Real
+ lightHeight : Real
<<ComplexAttributeType>> topmark
+ topmarkfitted : Boolean
+ topmarkcolor : Colour
+ topmarkshape : topmarkDaymarkShape
<<FeatureType>>
Light
+ lightCharacteristic : Text
+ categoryOfLight :CategoryOfLight
+ colour: Colour
+ lightQuality : Text
+ lightReachingDistance : Real
+ lensType : Text
+ lensStatus : Text
+ name : Text
+ id : Text
+ code : Text
+ installedDate : Date
+ surveyedDate : Date
includelight
0..1
includeAtoNAIS
0..1
position
1
daymark
1
daymark
1
AtoNAuthority 1
includeRacon 0..1

## Slide 2
<<FeatureType>>
AtoN
+ name : Text
+ id : Text
+ oode : Text
+ colour : Colour
+ shape : Text
+ establishedDate : Date
+ surveyedDate : Date
+ daymark : dayMark
+ position : GM_Point
<<FeatureType>>
Fixed_AtoN
+ altitude : Real
<<InformationType>>
AdministratingAuthority
+ organization : Text
+ country : Nationality
+ telephone : Text
+ email : Text
<<FeatureType>>
AtoNAIS
+ mmsiNumber : Integer
+ calculatedRange : Real
+ aisRxTx : AISRxTx
+ elevation : Real
+ status : Text
+ name : Text
+ id : Text
+ code : Text
+ installedDate : Date
+ surveyedDate : Date
<<FeatureType>>
Light
+ lightCharacteristics : Text
+ categoryOfLight : CategoryOfLight
+ colour : Colour
+ lightQuality : Text
+ lightReachingDistance : Real
+ lensType : Text
+ lensStatus : Text
+ name : Text
+ id : Text
+ code : Text
+ installedDate : Date
+ surveyedDate : Date
<<FeatureType>>
Racon
+ frequency : Real
+ power : Real
+ whistlingCycle : Text
+ name : Text
+ id : Text
+ code : Text
+ installedDate : Date
+ surveyedDate : Date
<<FeatureType>>
Beacon
+ islightfitted : Boolean
+ lightHeight : Real
<<FeatureType>>
LightHouse
+ lighthouseType : TypeOfLightHouse
+ height : Real
+ lightHeight : Real
<<FeatureType>>
SectorLight
+ mainlight : Light
+ lightHeight : Real
+ whiteSector : Angle
+ colouredSector : ColourSector
+ obsecuredSector : Angle
+ angleOfUncertainty : Angle
+ secondaryLight : Light
<<FeatureType>> Floating_AtoN
+ availabilityOfAtoN : PerformanceCriteria
<<FeatureType>>
Buoy
+ islightfitted : Boolean
+ bouytype : TypeOfBuoy
+ bouyshape : BuoyShape
<<FeatureType>>
LightVessel
+ lightHeight : Real
GM_Point
+ point
<<FeatureType>> dayMark
+ marktype: TypeOfMark
+ ialaRegion : TypeOfRegion
+ islightfitted : Boolean
+ lightRhythm: RhythmofLight
<<FeatureType>>
LightFloat
+ lightHeight : Real
<<ComplexAttributeType>> topmark
+ topmarkfitted : Boolean
+ topmarkcolor : Colour
+ topmarkshape : topmarkDaymarkShape
includelight
0..1
includeAIS
0..1
daymark
1
daymark
1
position 1
Position 1
includeRacon 0..1
AtoNAuthority 1

## Slide 3
<<Enumeration>>
RhythmOfLight
Fixed light
Occulting light
Single occulting light
Group occulting light
Composite group occulting light
Isophase light
Flashing light
Single flashing light
Long flashing light
…
<<Enumeration>>
IALARegion
Region A
Region B
Region A and Region B
Object diagram
1) Enumeration
<<Enumeration>>
Colour
White
Black
Red
Green
Blue
Yellow
Grey
Brown
Amber
…
<<Enumeration>>
BuoyShape
Conical
Cylindrical
Spherical
Pillar
Spar
Barrel
Super-buoy
Ice buoy
…
<<Enumeration>>
BuoyType
Cardinal Mark Buoy
Lateral Mark Buoy
Safe water mark buoy
Isolated danger mark buoy
Special mark buoy
Emergency Wreck marking buoy
Large navigational buoy
…
<<Enumeration>>
topmarkDaymarkShape
cone, point up
cone, point down
Sphere
2 spheres
cylinder (can)
Board
x-shape (St. Andrews cross)
upright cross (St. Georges Cross)
…
<<Enumeration>>
AvailiabilityOfFloatingAtoN
Category 1
Category 2
Category 3

## Slide 4
<<Enumeration>>
IALARegion
Region A
Region B
Region A and Region B
Object diagram
1) Enumeration
IALARegion:S100_GF_EnumerationType
+ enumerant = Region_A, Region_B, Region_AB
Region_A:S100_GF_Enumerant
+ code = 1
+ name = “Region_A”
+ definition = “IALA Region A”
+ domain = IALARegion
Region_B:S100_GF_Enumerant
+ code = 2
+ name = “Region_B”
+ definition = “IALA Region B”
+ domain = IALARegion
Region_AB:S100_GF_Enumerant
+ code = 3
+ name = “Region_AB”
+ definition = “IALA Region A and B”
+ domain = IALARegion

## Slide 5
name:S100_GF_SimpleAttributeType
+ memberName= name
+ definition =
+ valueType = CharacterString
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
Object diagram
2) AttributeType
- simple attribute type
id:S100_GF_SimpleAttributeType
+ memberName= id
+ definition = identification of an AtoN
+ valueType = CharacterString
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
code:S100_GF_SimpleAttributeType
+ memberName= code
+ definition = code of an AtoN
+ valueType = CharacterString
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
shape:S100_GF_SimpleAttributeType
+ memberName= shape
+ definition = description about the shape of an AtoN
+ valueType = CharacterString
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
establishedDate:S100_GF_SimpleAttributeType
+ memberName= establishedDate
+ definition = Date that an AtoN is established
+ valueType = Date
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
surveyedDate:S100_GF_SimpleAttributeType
+ memberName= surveyedDate
+ definition = date that an AtoN is surveyed
+ valueType = CharacterString
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]

## Slide 6
topmarkfitted:S100_GF_SimpleAttributeType
+ memberName= topmarkfitted
+ definition = attribute for checking a topmark is fitted
+ valueType = Boolean
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
Object diagram
2) AttributeType
- complex attribute type
topmark:S100_GF_ComplexAttributeType
+ memberName= topmark
+ definition = a set of attributes for describing a topmark
+ valueType = CharacterString
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
+ carries : topmarkfitted, topmarkcolour, topmarkshape
topmarkcolour:S100_GF_SimpleAttributeType
+ memberName= topmarkcolour
+ definition = attribute for describing colour of a topmark
+ valueType = EnumerationType
+ domain = Colour
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]
topmarkshape:S100_GF_SimpleAttributeType
+ memberName= topmarkshape
+ definition = attribute for describing shape of a topmark
+ valueType = EnumerationType
+ domain = topmarkDaymarkShape
+ domainOfValues =
+ multiplicity : S100_multiplicity [0..1]

## Slide 7
lightSource:S100_GF_AssociationType
+ typeName = “”
+ definition = “”
+ includes = “Light”, “AtoN”,
+ roleName = “includelight”, “lightAttachedTo”
Object diagram
3) AssociationType and Association Roles
includelight:S100_GF_AssociationRole
+ memberName= includelight
+ definition = “a role for representing an AtoN includes a light”
+ multiplicity : S100_multiplicity [0..*]
lightAttachedTo:S100_GF_AssociationRole
+ memberName= lightAttachedTo
+ definition = “a role for representing a light to be attached”
+ multiplicity : S100_multiplicity [0..1]

## Slide 8
Buoy:S100_GF_FeatureType
+ typeName = S100_GF_FeatureType
+ definition = “”
+ isAbstract = False
+ linkbetween = “lightSource”
+ carrierOfCharacteristics = name
+ carrierOfCharacteristics = id
+ carrierOfCharacteristics = code
+ carrierOfCharacteristics = colour
+ carrierOfCharacteristics = shape
+ carrierOfCharacteristics = establishedDate
+ carrierOfCharacteristics = surveyedDate
+ carrierOfCharacteristics = availabilityOfAtoN
+ carrierOfCharacteristics = daymark
+ carrierOfCharacteristics = position
+ carrierOfCharacteristics = islightfitted
+ carrierOfCharacteristics = includelight
+ carrierOfCharacteristics = bouytype
+ carrierOfCharacteristics = bouyshape
Object diagram
4) FeatureType
Light:S100_GF_FeatureType
+ typeName = S100_GF_FeatureType
+ definition = “”
+ isAbstract = False
+ linkbetween = “lightSource”
+ carrierOfCharacteristics = name
+ carrierOfCharacteristics = id
+ carrierOfCharacteristics = code
+ carrierOfCharacteristics = establishedDate
+ carrierOfCharacteristics = surveyedDate
+ carrierOfCharacteristics = lightCharacteristic
+ carrierOfCharacteristics = lcategoryOfLight
+ carrierOfCharacteristics = lightType
+ carrierOfCharacteristics = colour
+ carrierOfCharacteristics = lightQuality
+ carrierOfCharacteristics = lightReachingDistance
+ carrierOfCharacteristics = lensType
+ carrierOfCharacteristics = lensStatus
+ carrierOfCharacteristics = lightAttatchedTo