## Slide 1: How can IALA adopt S-100 for Product Specifications?
Ministry of Land, Transport, and Maritime Affairs
Republic of Korea

## Slide 2: Agenda
Introduction to IHO S-100
Roles of IALA as a domain owner
Development Procedure of Product Specification
Issues and Open Questions

## Slide 3: Introduction to S-100

## Slide 4: S-100
S-100 is a Universal data model for hydrographic data.
  IHO’s standard
  S-100 is the guideline for ‘Product Specification’, which is, in turn, the guideline for data product production and distribution.
  S-100 has been agreed among international bodies including IMO, IHO and IALA as the baseline for the Common Maritime Data Structure required for e-Navigation.
Notes: S-100에 대한 개념적 설명.

## Slide 5: S-100, S-10x, and Data Products
S-100
S-101 ENC Product Specification
S-102 Bathymetry
Product Specification
S-10x AtoN Product Specification
en.wikipedia.org
en.wikipedia.org
Navguide 2010
…
Notes: Universal data model인 S-100, 각 데이터에 대한 product specifications, 실제 데이터셋인 (data products)의 개념과 관계를 설명.

## Slide 6: Contents of S-100
Management of IHO Geospatial Information Registers
Feature Concept Dictionary Registers
General Feature Model and Rules for Application Schema
Metadata
Feature Catalogue
Coordinate Reference Systems
Spatial Schema
Imagery and Gridded Data
Portrayal
Encoding Formats
Product Specifications

## Slide 7: Registry
IHO runs GI1) Registry, which helps management and development of Product Specifications.
  Registry is used for easy access and management of Common terms, domain specific feature definition, portrayal, product specification version.
  http://registry.iho.int
1) GI : Geographic Information
IHO GI Registry
Feature Concept Dictionary
Register
Portrayal
Register
Metadata
Register
Product Specification Register
Data Producer
Codes
Register

## Slide 8: IHO GI Registry
5 Register types

## Slide 9: IHO GI Registry
Hydro, Inland ENC, ICE,,, (Domains)
Hydrographic domain’s feature list. Features’ attributes are not defined here.

## Slide 10: Roles of IALA as a domain owner

## Slide 11: E-Navigation and IALA domain’s product specifications
Needs for developing Product Specifications for IALA domain?
  S-100 provides a fundamental framework that facilitates integration among various domains.
  In a case, such as e-navigation, where we want integrate several domain data products to provide a coherent service,
  Each domain’s data products should be developed by experts on that domain based on S-100.
Notes: e-Navigation should enable the
mariner to access more, relevant
information
• Information will need to be
organised and presented clearly
• Standardised, interoperable and
18
unambiguous presentation
• Processing and presentation
systems with particular attention
to HMI, to avoid overload

## Slide 12: IALA domain
IALA domain
  IALA is the expert on aids to navigation issues.
  IALA should be working as the domain owner.
AtoN
AIS
IVEF
IALA domain
…
Notes: IALA 도메인의 도메인 전문가로서의 IALA의 역할
Registry에서의 도메인 owner의 역할

## Slide 13: Proposal for a new Domain
Notes: Feature Concept Dictionary에 새로운 아이템의 등록을 신청하는 폼.

## Slide 14: IALA as a Domain Owner
Propose and manage Product Specifications in the domain.
(obviously) Manage IALA domain in IHO Registry.
Be the authority of S-100 for IALA (I’ll talk about this later.)
Notes: e-Navigation should enable the
mariner to access more, relevant
information
• Information will need to be
organised and presented clearly
• Standardised, interoperable and
18
unambiguous presentation
• Processing and presentation
systems with particular attention
to HMI, to avoid overload

## Slide 15: Product Specification
Notes: Product Specification에 대해 개념적으로 설명하고,
특정 도메인의 Product Specification을 개발하는 과정을 설명한다.
그리고, IALA 도메인의 ANM을 대상으로 Product Spec을 개발하는 과정에서 고민했던 사항들에 대해서 설명한다.

## Slide 16: Product Specification
Product specification
  It defines guidelines for data product (data set) development and deployment for a certain domain.
    To do this, it defines terms for domain data, data contents and structure, data elements and portrayal, data set deployment format.
    During Product Specification development process, registers in the GI registry are referenced.
Notes: S-100 설명 과정에서 Product Specification의 개념 설명이 이루어짐. (중복?)
S-100 기반 Product Specification의 구성에 초점을 맞추어 설명?

## Slide 17: Typical Components of Product Specification
General Feature Model
FCD Register
Portrayal
Product Specification
Metadata
Product Spec.
Producer
Code
Application Schema
Feature Catalogue
Portrayal Catalogue
Encoding Format
GI Registry
Metadata
FCD Register
Portrayal
Metadata
Product Spec.
Producer
Code
FCD
Portrayal
Metadata
Product Spec.
Producer
Code

## Slide 18: Product Specification Development Process (1)
Decide the domain to make data product for
Register the terms on commonly managed dictionary *
Understand characteristics of the domain data
(Feature-based vs. Coverage data)
Find and organize terms used for the domain
* FCD register
Preprocessing Steps

## Slide 19: Product Specification Development Process (2)
Common Terms Dictionary
(FCD Register)
Symbol, Portrayal guideline
(Portrayal Register)
Define data elements thoroughly
Define portray rules for data element
Registers in the GI Registry
Feature Catalogue(1)
Portrayal Catalogue
Define relationship among data elements and data structures(2)
General Feature Model
(1) in-depth explanation of elements of data
(2) Application Schema

## Slide 20: Product Specification Development Process (3)
Additional processes
Define identification method for data set
Data set explanation metadata definition
Data set deployment format definition

## Slide 21: Case study
Notes: Product Specification에 대해 개념적으로 설명하고,
특정 도메인의 Product Specification을 개발하는 과정을 설명한다.
그리고, IALA 도메인의 ANM을 대상으로 Product Spec을 개발하는 과정에서 고민했던 사항들에 대해서 설명한다.

## Slide 22: AtoN Product Specification
Korea developed Remote monitoring & controlling AtoN Management system.
It follows domestic standards.
Need for making it S-100 based.
References
  Integrated AtoN Management system
  IALA’s Navguide (2010 edition)
  AtoN Information Metadata product specification(e-Nav11-17-9)

## Slide 23: AtoN Product Specification
Category | IALA Item | Domestic | IHO Hydro domain
fixed AtoN | Lighthouse staffed facility, automated facility | Lighthouse - manned lihgthouse, unmanned lighthouse | 
 | Beacon | Beacon - light beacon, standing beacon | Beacon, cardinal Beacon, isolated danger Beacon, lateral Beacon, safe water Beacon, special purpose/general
Floating AtoN | Buoy | Buoy - light buoy, buoy | Buoy, cardinal Buoy, installation Buoy, isolated danger Buoy, lateral Buoy, safe water Buoy, special purpose/general
 | Lightvessel | - | Lightvessel
 | Lightfloat | - | Lightfloat
 | LANBY(large navigational buoy) | - | 
Marks | Lateral Mark | - | Daymark, Topmark
 | Cardinal Mark | - | 
 | Isolated Danger Mark | - | 
 | Safe Water Mark | - | 
 | Special Mark | - | 
- | Light | Light - fixed direction light, leading light, bridge light | Light - attribute : category of light
 | Sector Light |  | 
 | Leading (Range) Lines |  | 
 | Racon | Racon | Radar transponder beacon - attribute: category of radar transponder beacon
 |  | Lantern | 
 |  | Electronic horn | 
 |  | DGPS station | Radio station - attribute : category of radio station

## Slide 24: ISSUES & QUESTIONS
Ambiguous statements in S-100.
Whose Domain does this belong?

## Slide 25: ISSUES & QUESTIONS S-100 Ambiguity (1)
All classes used within an application schema for data transfer shall be instantiable.
– from S-100 Application Schema Main Rules

## Slide 26: ISSUES & QUESTIONS S-100 Ambiguity (2)
All classes used within Application Schema shall be instantiable.
Additionally, Application Schema is for data transfer. (‘for data transfer’ qualifies Application Schema)

## Slide 27: ISSUES & QUESTIONS S-100 Ambiguity (2)
Means,
All classes we are modeling should be concrete (non-abstract).

## Slide 28: ISSUES & QUESTIONS S-100 Ambiguity (3)
Among the classes within Application Schema,
all classes used for data transfer shall be instantiable.

## Slide 29: ISSUES & QUESTIONS S-100 Ambiguity (3)
Means,
Those classes used for data transfer should be concrete.
There can be classes that are not for data transfer in Application Schema, thus can be abstract.

## Slide 30: ISSUES & QUESTIONS S-100 Ambiguity (4)
We want consistency among IALA’s different Product Specifications.
A source for definitive & authoritative answers to this type of questions would be great.
Notes: AIAL’s own or IHO’s

## Slide 31: ISSUES & QUESTIONS Whose Domain does this belong?
  During the product specification development process, we’ve found a few features that were already registered in other domains.
  What do we do we found such a feature?
  Use them as they are?
  Modify it and register as a new version?
  Just put a (possible) duplication?
  And who’s feature ‘buoy’ is anyway? 
Notes: 프로덕트 스펙을 개발하는 중에 특정 피처(예 buoy)가 유사한 형태로 다른 도메인에 포함되어 있는 경우가 있었다.
이 경우에 유사한 피처들을 그대로 사용할 것 인지? 새로운 피처를 수정해서 사용할 것인지? 중복해서 registry에 등록할 것인지?를 결정해야 한다.
이를 위한 가이드라인 등의 일을 해야한다.

## Slide 32: ISSUES & QUESTIONS Other modeling issues
Issues on ANM domain’s Feature type, Attribute type definition process
  Different ways for Feature type class definition
    ‘Buoy’ feature type - Different classes for different types of buoys? Or, One general class with an attribute that represents its type?
    example)
      ‘Buoy’ : (a class per type)
        Buoy, cardinal ; Buoy, installation ; Buoy, isolated danger
        Buoy, lateral ; Buoy, safe water ; Buoy, special purpose/general
      ‘Radar transponder beacon’
        ‘category of radar transponder beacon’ (type representing attribute used)

## Slide 33: ISSUES & QUESTIONS Other modeling issues
Issues on ANM domain’s Feature type, Attribute type definition process
  Attribute type definition
    When attributes type name is same as IHO domain’s attribute element,
      Identify that the attribute type is identical to the existing attribute element By figuring out what attribute element means. ex) ‘elevation’
    When there is a attribute element with similar concept but with different name
      ex1) ‘elevation’ vs. ‘altitude’
      ex2) ‘methodOfSurvey’ vs. ‘surveyType’

## Slide 34: ISSUES & QUESTIONS Other modeling issues
Issues on Feature Catalogue developing process
  There can be more than one way to define the same real world phenomenon as a feature depending on domain.
    ex) Racon
      IHO hydro domain Setting category of radar transponder beacon attribute of radar transponder beacon to 1 makes it ‘Racon’
      IALA domain
      Define ‘Racon’ feature type class
  How do we recognize these features that are defined in different ways but indicating the same thing as identical feature in e-Navigation context?
    IALA domain’s ‘Racon’ and IHO domain’s ‘Radar transponder beacon’ feature

## Slide 35
Thank you!