## Slide 1: The Notion of “Maritime Service Portfolio(s) (MSP)” – a strategic key for international/global harmonization of shore-based services offered to shipping
Jan-Hendrik Oltmann, Germany
+
Jarle Hauge, Norway

## Slide 2: Presentation overview
Background and “Definitions”
MSPs and the overarching e-Navigation architecture
Shipboard equipment / INS and the MSP
Areas, Stakeholders, Hierarchies
Common Maritime Data Structure (CMDS)
e-Navigation „products“
Foreseen next steps for IALA’s work (IALA MSP “road map”)
Notes: <number>

## Slide 3: Background and “Definitions“
* Report of „e-Navigation Correspondence Group“ (NAV56/8), 23 April 2010
Paradigm
MSP / Levels
Onboard- Ashore
Notes: <number>

## Slide 4
Maritime services:
Meaning:
  to provide defined assistance to maritime actors
Varieties of maritime services include:
  Operational
  Technical
  Commercial
will have
  level(s) of service
  service parameters
A Maritime Service Portfolio is a set of services.
There will be different MSPs for different areas.
Background and “Definitions“
Notes: <number>

## Slide 5
* IMO MSC85/26, Annex 20, 4, MSC-adopted 2008
Shipboard
Shore-based
Communications
Maritime Service Portfolio(s)
MSP and the overarching e-Navigation architecture

## Slide 6
* IMO NAV57, WP6, Fig. 1
TECHNICAL Services
Maritime Service Portfolio
OPERATIONAL Services
MSP and the overarching e-Navigation architecture – Zoom-In
Zoom-In: shipboard side

## Slide 7
Service N
Service 2
Service 1
Shore systems of MSP service providers
etc.
INS
Module
Radio
Links
Shipboard
Shore-based
The Integrated Navigation System (INS) is the core element of the „shipboard technical equipment supporting e-Navigation“.
„Maritime Service Portfolio (MSP)“
Training
etc.
Modul A
Modul B
Modul C
Module
D
Alarm Management Module
Module X
Consistent Common Reference System CCRS
Integrated Navigation System
MSP and the overarching e-Navigation architecture – Zoom-In: Shipboard side.

## Slide 8
Ship-side
Shore-side
Links
I N S Integrated Navigation System
+
M S P Maritime Service Portfolio
Shipboard equipment / INS and the MSP

## Slide 9
Ship-side
Shore-side
Links
I N S Integrated Navigation System
M S P Maritime Service Portfolio
Shore side requirements; defined and known ship equipment
Shipboard requirements; reliable and continuous services from ashore
Shipboard equipment / INS and the MSP

## Slide 10
S<number>
Integrated Navigation System
Maritime
Service Portfolios
Requirements
endorsed by IMO
Common Maritime Data Structure
* IALA, e-NAV9-output-3; March 2011
Shipboard equipment / INS and the MSP
Notes: <number>

## Slide 11
Ocean - Transocean Voyage
Harbour
Harbour
A
B
Coastal
Coastal
Arctic area
Remote area
Offshore
Different MSPs in different areas

## Slide 12
* IMO MSC85/26, Annex 20, Attachment, MSC-adopted 2008
Services
Different Stakeholders provide MSP(s)

## Slide 13
Global scope: Common, generic and unique/unified MSP definition for all relevant sea areas + minimum requirements regarding service provision and participation (e.g IMO, IHO, IALA, IMPA, …)
Regional scope: Additional regional MSP definition + additional minimum requirement?! (e. g. in Europe: „e-Services“ by 2018 (EU-KOM at NAV57) ?)
National scope: Additional national MSP definition + provision of internationally and regionally required MSPs for coastal areas (e. g. Germany or Norway)
Local scope: Additional local MSP definition + provision of internationally, regionally, and nationally required MSPs for port areas(e. g. Ports)
Different scopes of services / MSPs – hierarchy of MSPs

## Slide 14
S<number>
Integrated
Navigation
System
Maritime
Service
Portfolios
Requirements
endorsed by IMO
Common Maritime Data Structure (CMDS)
* IALA, e-NAV9-output-3; March 2011
Common Maritime Data Structure (CMDS)
Notes: <number>

## Slide 15
S<number>
MSP(s)
Service(s)
System(s)
Component(s), Data Interface(s)
Data => CMDS
Common Maritime Data Structure (CMDS)
Notes: <number>

## Slide 16
  CMDS = the „glue“ for „e-Navigation“:
  Common reference for definition and description of
  data within the framework of „e-Navigation“.
  CMDS is based on IHO Registry
    (IHO Standards S-100/S-99 as a „baseline“)
  IMO/IHO Harmonization Group on Data Modelling (HGDM):
Terms of Reference (NAV58) =>
adopted by MSC 90 (May2012)!
start after MSC 91 (November 2012).
Common Maritime Data Structure (CMDS)
Notes: <number>

## Slide 17
S<number>
* IMO NAV57 WP.6; Juni 2011
IHO Registry
Common Maritime Data Structure (CMDS)
Notes: <number>

## Slide 18
S<number>
„Product“ as a service
* IMO NAV57 WP.6; Juni 2011
E-Navigation “products”
Notes: <number>

## Slide 19
S<number>
  Operational Services:
        Well-known services, as projected into the MSP paradigm
        New services ?! (e. g. AIS ASM descriptions of IMO SN.1/Circ.289)
  Technical Services:
        Well-known services, as projected into the MSP paradigm
        New services ?! (again such as those implied by the above AIS ASM descriptions)
  Component descriptions
  Human Machine Interface descriptions
  Data exchange interface descriptions
  Data modeling for „signal-in-space“ decriptions
E-Navigation “products”
Notes: <number>

## Slide 20
S<number>
  Further develop („zoom-in“) framework description for MSPs, including, amongst others, the „product“ notion
  Collect existing operational and technical services and their service levels / parameters
  Introduce existing services into MSP framework and determine need for clarification / further definition (= „migration“ of existing services)
  Identify required new services and introduce them into MSP framework
  Introduce data requirements from „products“ into emerging Common Maritime Data Structure (CMDS)
  Further develop generic description of shore-based services (technical description)
Foreseen next steps for IALA’s work – “the IALA MSP road-map”
Notes: <number>

## Slide 21
The following slides are meant to provide additional information on the work of IALA e-Navigation Committee in regard the requirements for the „shipboard equipment supporting e-Navigation“ as seen from ashore.
The following slides will be shown should there be a discussion leading towards that topic.
Spare slides follow.

## Slide 22
PNT Sensors
Depth sensor
Radar Sensor(s)
Sensor/ Source Layer
using CMDS
Consistent Common Reference System
PNT evaluation
System Data
selection
Integrated Radio Communication
VHF
Radio Resource Management (selection, filtering, routing, signaling and alerting)
Collision avoidance
Route planning and monitoring
Navigation Control (incl. Track Control)
Alert manag.
Other bridge systems
Integrated Navigation System (INS)
Data Processing Layer
Operational Layer, incl. provision of HMIs
Status and Data Display
Active INS Data base (Route information, SENC, Hydrographical, Weather,…)
BAM
INS Communication
Safety
…
Interface to external systems
SAT
Vessel parameters
Static data, pre-packed (e.g. ENC data)
Dynamic / real-time data
AIS
…
…
HF
MF
LF
…
* Annex to the Report of the IMO e-NAV Correspondence Group to NAV 58; April 2012
Zoom-In: Shipboard side.
Notes: <number>

## Slide 23
“There is defined a generic shipboard technical architecture in functional terms as an architectural and design reference.”
“This shipboard architecture includes state-of-the-art concepts.”
  hierarchical functional layers
  a modular concept
  flexible interface sentence semantics
“It is noted that IMO has created the INS Performance Standards and associated guidelines. That modular Integrated Navigation System (INS) is therefore considered as the architectural framework for the shipboard technical architecture.”
(compare figure on following slide as an example, as prepared by the German Institute of Navigation (DGON))
* IALA e-NAV Committee Working Paper, March 2012
Preliminary requirements for shipboard equipment (as seen from ashore)
Notes: <number>

## Slide 24
“There are further defined additional modules for the shipboard functional architecture, in particular regarding the radio communications.”
  module tentatively called “Integrated Radio Communication”.
“A Capability Negotiation functionality is required for the shipboard INS and the Integrated Radio Communication.”
  “This functionality interacts with the shore side and provides the shore side with information about the capabilities of the shipboard electronic environment. This in turn is used by the shore side to tailor the data exchange with the shipboard electronic environment to the functionalities supported on board.”
* IALA e-NAV Committee Working Paper, March 2012
Preliminary requirements for shipboard equipment (as seen from ashore)
Notes: <number>

## Slide 25
“A concern is the present integrity, consistency and quality of information/data received.”
  “Integrity, consistency and quality is improved by taking into account the data transaction chain(s) from initial shipboard source(s) of the data, through the different stages, to the transmission point(s) ship to shore /ship to ship, as a whole. This principle applies also to the communications shore to ship, as appropriate. The shipboard e-Navigation environment uses the Common Maritime Data Structure (CMDS), thus fulfilling this requirement.”
“The resulting requirements from the shipboard e-Navigation environment to the CMDS, to the IHO Registry based on S-100 and to the technical services contributing to the Maritime Service Portfolios (MSP) are defined and brought to the attention of the appropriate stakeholders.”
* IALA e-NAV Committee Working Paper, March 2012
Preliminary requirements for shipboard equipment (as seen from ashore)

## Slide 26
“Unique technical identifiers to achieve the above integrity goals are defined, elaborated and published.”
“In order to maintain the integrity and quality, a flexible, safe and secure update management process for shipboard equipment are established and applied.”
* IALA e-NAV Committee Working Paper, March 2012
Preliminary requirements for shipboard equipment (as seen from ashore)