## Slide 1
Overview
Dates: 21 Oct. 2007 – 16 Nov. 2007 (4 weeks)
Venue: CICG & ITU HQ (Geneva)
Participants: 2,800 people from 164 countries
Report on WRC-07
Agenda related to Maritime Mobile Service
Agenda Item 1.13 - Review of frequency allocation in the band 4-10MHz
Agenda Item 1.14 - Review of operational procedures and requirements of GMDSS
Agenda Item 1.16 - MMSI assignment to equipment other than shipborne equipment

## Slide 2
Agenda Item 1.13
Review of frequency allocation in the band 4-10MHz
Main Issue
Additional spectrum allocation to Broadcasting Service
  (350-800kHz total in the band 4-10MHz)
  Candidate spectrums – Fixed & Land Mobile services
  Spectrum compensation
  Non channelized frequencies in Appendix 17 for Maritime Mobile service
CEPT
APT
CITEL
RCC
  Candidate spectrums
Supported
Objected
confrontation
Results
No additional spectrum allocation to Broadcasting Service
No change to frequency allocation Table in RR Article 5
Revise Appendix 17 at WRC-11
Notes: <number>
CEPT: European Conference of Postal and Telecommunications Administrations
APT: Asia Pacific Telecommunity
CITEL: Inter-American Telecommunication Commission
RCC: RCC: Regional Commonwealth in the field of Communication

## Slide 3
Agenda Item 1.14 (1/3)
Review of operational procedures and requirements of GMDSS
Suppression of Appendix 13
  non-GMDSS distress and safety communication procedures by voice
    VHF procedures RR Articles 32/33
    MF/HF procedures New Resolution 354 [COM4/3]
  Radio Operators Certificate RR Article 47
Modification of Appendix 15 (Frequencies for GMDSS)
AIS-SART frequencies (AIS1, AIS2) incorporated by CITEL proposal
* Except as provided in these Regulations, any emission capable of causing harmful interference to the frequencies denoted by an asterisk (*) is prohibited.

## Slide 4
Agenda Item 1.14 (2/3)
Review of operational procedures and requirements of GMDSS
Protection of VHF CH70
Modification of frequency allocation table in RR Article 5
Results
5.227 Additional allocation: the bands 156.4875-156.5125 MHz and 156.5375-156.5625 MHz are also allocated to the fixed and land mobile services on a primary basis. The use of these bands by the fixed and land mobile services shall not cause harmful interference to nor claim protection from the maritime mobile VHF radiocommunication service. (WRC-07)

## Slide 5
Agenda Item 1.14 (3/3)
Review of operational procedures and requirements of GMDSS
Modification of Appendix 18 (major items)
Modified footnotes
  f) AIS1 and AIS2 may also be used by aircraft stations for the purpose of search and rescue operations and other safety-related communication.
  l) AIS1 and AIS2 are used for an automatic identification system (AIS) capable of providing worldwide operation, unless other frequencies are designated on a regional basis for this purpose. Such use should be in accordance with the most recent version of Recommendation ITU-R M.1371.
  o) These channels may be used to provide bands for new technologies, subject to coordination with affected administrations. Stations using these channels or bands for new technologies shall not cause harmful interference to, and shall not claim protection from, other stations operating in accordance with Article 5. The design of such systems shall be such as to preclude the possibility of interference to the detection of AIS signals on 161.975 or 162.025 MHz.
Added footnotes
  p) Additionally, AIS 1 and AIS 2 may be used by the mobile-satellite service (Earth-to-space) for the reception of AIS transmissions from ships.
  q) When using channels 10 and 11, all precautions should be taken to avoid harmful interference to channel 70.

## Slide 6
Agenda Item 1.16
MMSI assignment to equipment other than shipborne equipment
Another proposal by Mexico: Increase station types to reserve MID resource
  SAR ship station: 10MIDXXXX SAR aircraft station: 11MIDXXXX
  GMDSS Coast Station: 00MIDXX(1-5)0 VTS Coast Station: 00MIDXX(6-7)0
  SAR Station: 00MIDXX(8-9)0
  AtoN Group Station: 00MIDXX00 AtoN Buoy: 00MIDXXX(1-9)
Modification of RR Article 19
  describes the same text of Rec. M.585-4 (Method A)
or
  refers to the Rec. M.585-4 (Method B)
CEPT
APT
CITEL
Support
Support
should be considered in Study Group future revision of Rec. M.585-4
majority supported Method B
Modified RR Article 19 by Method B

## Slide 7
New Agendas for WRC-11
Related to Maritime Mobile Service
Agenda Item 1.9 Revision of Appendix 17 for implementation of new digital technology (HF data communications)
Agenda Item 1.10 Examination of frequency allocation for Ship and Port Safety System  additional channels for Maritime Mobile Service and Mobile Satellite Service (AIS)
Agenda Item 1.14 VHF Radiolocation Service (VHF Radar for space debris detection using 30-300MHz) possibility of interference to AIS and VHF distress channels
Agenda Item 1.15 Possible allocations to HF radio location Service in 3-50MHz (HF oceanographic radar)
Agenda Item 1.23 Possible allocation of 15kHz in 415-526.5kHz to Amateur Service on secondary basis  possibility of interference to NAVTEX service

## Slide 8
Restructure of ITU-R Study Groups
Result of RA (Radiocommunication Assembly)
Study Group 1 (SG 1) - Spectrum management
Study Group 3 (SG 3) - Radiowave propagation
Study Group 4 (SG 4) - Satellite services
Study Group 5 (SG 5) - Terrestrial Services
- Working Party 5A (WP 5A) - Land mobile service excluding IMT; amateur
  and amateur-satellite service
  - Working Party 5B (WP 5B) - Maritime mobile service including Global
  Maritime Distress and Safety System (GMDSS); aeronautical mobile service and radiodetermination service
  - Working Party 5C (WP 5C) - Fixed wireless systems; HF systems in the Fixed and Land Mobile Services
  - Working Party 5D (WP 5D) - IMT Systems
Study Group 6 (SG 6) - Broadcasting service
Study Group 7 (SG 7) - Science services