## Slide 1: COMPASS/Beidou Navigation Satellite System Development
GNSS Navigation Center of Dalian Maritime University
Jun. 8th-12th, 2009, St Germain-en-Laye France
1
E-NAV7/19/4

## Slide 2: Contents
1. Basic principles of the State Policy
2. System General Description
3. System Deployment
4. Compatibility and Interoperability
5. The International Maritime Standards
2

## Slide 3
The contents in the presentation are from “ China Satellite Navigation Project Center ”.
China decided to build an independent satellite navigation system in 1980’s.
In 2003, the COMPASS/Beidou navigation demonstration system was built and has been used in many areas.
Now the COMPASS/Beidou global navigation system is under construction.
3

## Slide 4: Principles of the State Policy
Openness
Independency
Compatibility
Gradualness
4

## Slide 5: Principles of the State Policy
Openness
COMPASS/Beidou will provide high quality public services free of direct user charge, and we encourage the applications of COMPASS/Beidou all over the world.
China will communicate with other countries widely and deeply in the field of satellite navigation to promote compatibility and interoperability among GNSS, and push the advancement of world satellite navigation technology and industry.
5

## Slide 6: Principles of the State Policy
Independency
China will develop and operate COMPASS/ Beidou system independently. COMPASS/Beidou can provide services for users and higher quality services in Asia-Pacific region independently.
6

## Slide 7: Principles of the State Policy
Compatibility
COMPASS/Beidou will pursue solutions to realize compatibility and interoperability with other satellite navigation systems, and users can get better services with interoperable receivers. Based on the protection of current users and industry, all users will enjoy the improvement of COMPASS/Beidou navigation satellite system.
7

## Slide 8: Principles of the State Policy
Gradualness
In order to control the technical and economic risks, COMPASS/Beidou will be developed step by step based on technology and economy level of China.
And COMPASS/Beidou will provide long-term continuous services for users, and incessantly improve system performance to realize seamless link and smooth transition of every phase.
8

## Slide 9: Contents
1. Basic principles of the State Policy
2. System General Description
3. System Deployment
4. Compatibility and Interoperability
5. The International Maritime Standards
9

## Slide 10: Principles of the State Policy
System structure
Signal Characteristics
Time System
Coordinate System
Services and Performances
10

## Slide 11: System Structure
Space Segment
5 GEO and not more than 30 MEO satellites
Constellation
11
GEO Satellite
MEO Satellite
Notes: <number>

## Slide 12: System Structure
Ground Segment
The ground segment consists of Master Control Station, Upload Stations and Monitor Stations.
12
Notes: <number>

## Slide 13: System Structure
User Segment
The user segment consists of COMPASS/Beidou user terminals and interoperable terminals.
13
User terminals of COMPASS/Beidou system
Notes: <number>

## Slide 14: Signal Characteristics
Frequencies
B1, B2, B3
Signals:
B1(QPSK), B1-MBOC , B1-2 (QPSK),
B2(QPSK), B2-BOC
B3(QPSK), B3-BOC
L5 (QPSK).
14

## Slide 15: Signal Characteristics
COMPASS/Beidou time named as BDT, traced to UTC, and be synchronized with UTC in 100ns. The epoch time of BDT is UTC 00d 2006.
Interoperability of BDT with GPS/Galileo time is considered in the design of COMPASS/Beidou time system. The offset between BDT and GPST/ GST will be measured and broadcast.
15

## Slide 16: Signal Characteristics
COMPASS/Beidou coordinate system is named as China Geodetic System (CGS2000).
Coinciding with ITRF at few cm level, and for most applications the difference between CGS2000 and ITRF can be neglected.
16

## Slide 17: Services and Performances
Two kinds of global services
Open Service：free and open to users
Positioning Accuracy: 10 m (2σ)
Timing Accuracy: 20 ns
Velocity Accuracy: 0.2 m/s
Authorized Service: ensure highly reliable use even in complex situation.
17

## Slide 18: Services and Performances
Two kinds of regional services:
Wide area differential service
Positioning accuracy: 1 m (2σ)
short message service.
18

## Slide 19: Contents
1. Basic principles of the State Policy
2. System General Description
3. System Deployment
4. Compatibility and Interoperability
5. The International Maritime Standards
19

## Slide 20: System Deployment
Deployment Step
Launch schedule
COMPASS-M1 Experimentation
20

## Slide 21: Deployment Step
1st Step—Demonstration System
21
After 3 GEO satellites launched since 2000, the demonstration system can provide basic services including positioning, timing and short-message telecommunication in regional area.
Notes: <number>

## Slide 22: Deployment Step
2nd Step—Global System
COMPASS/Beidou will cover Asia-Pacific area firstly about 2010, and will cover all over the world about 2015 to 2020.
About 2010
About 2015 to 2020
22
Notes: <number>

## Slide 23: Deployment Step
23
The first MEO satellite was launched in Apr. 2007.
Notes: <number>

## Slide 24: Launch Schedule
24
Planed launches in recent two years
During 2009, 3-4 satellites will be launched, and more than 10 satellites will be put into use in recent two years by Long-March launchers. About 2010, the system can offer services regionally.

## Slide 25: COMPASS-M1 Experimentation
25
Rubidium Atom Frequency Standard
4 RAFS has been operating continuously for 18 months. The test results showed that the RAFS worked normally and the performance satisfied the design requirements.

## Slide 26: COMPASS-M1 Experimentation
26
Orbit determination and Time synchronization
Orbit determination precision: < 5 m
Orbit prediction precision : < 10 m (24 hours)
Time synchronization precision: < 2ns

## Slide 27: Contents
1. Basic principles of the State Policy
2. System General Description
3. System Deployment
4. Compatibility and Interoperability
5. The International Maritime Standards
27
Contents

## Slide 28: Compatibility and Interoperability
28
Comprehension on Compatibility and Interoperability
Related Bilateral Activities

## Slide 29
29
Compatibility: the ability of multiple satellite navigation system services to be used separately or together, without the generated interference to affect the navigation performance of each system.
Interoperability: the ability of multiple satellite navigation system services to be used together to provide better capabilities at the user level than would be achieved by relying solely on one service or signal, without significantly increasing the complexity of receivers.

## Slide 30: Related Bilateral Activities
30
Three frequency compatibility coordination meetings:
COMPASS and GPS:
The 1st Meeting was held in Geneva in June 2007.
The 2nd Meeting was held in Xi’an in May 2008.
The 3rd Meeting was held in Geneva in Oct 2008.

## Slide 31: Related Bilateral Activities
31
The 1st frequency compatibility coordination meeting was held in Beijing in May 2007.
The 1st Technical Working Group (TWG) meeting on
Compatibility and Interoperability was held in Beijing in Sep 2008.
The 2nd TWG meeting on Compatibility and Interoperability was held in Beijing in Dec 2008.
COMPASS and GALILEO:

## Slide 32: Related Bilateral Activities
32
The frequency compatibility coordination meeting was held in Moscow in Jan 2007.
COMPASS and GLONASS:

## Slide 33
33
The development of COMPASS/Beidou is a national strategy of China.
COMPASS/Beidou is an essential element of the international GNSS.
COMPASS/Beidou is being constructed efficiently and smoothly.
China encourages international cooperation to ensure compatibility and interoperability with other navigation systems.

## Slide 34: Contents
1. Basic principles of the State Policy
2. System General Description
3. System Deployment
4. Compatibility and Interoperability
5. The International Maritime Standards
27
Contents

## Slide 35: Maritime Standards
5. The International Maritime Standards
As one of the GNSS members in the world, COMPASS will establish the international maritime standards which deal with some international organizations such as IMO, ITU, IEC, RTCM and etc., just like GPS, GLONASS, and GALILEO have done.
So in IALA documents COMPASS will be dealt with, such as in e-NAV6 final report “ ANNEX 7 REVISED WORK PROGRAMME AND TASK PLAN FOR 2006-2010”, the “M3 Developments in GNSS – Galileo, GLONASS K, GPS 3 ” may be changed as “M3 Developments in GNSS – Galileo, GLONASS K, GPS 3, COMPASS ”.
2

## Slide 36
34
Thanks
for your attention!